STATE OF MISSISSIPPI

OKTIBBEHA COUNTY

ADVERTISEMENT FOR BID PROPOSALS

MISCELLANEOUS COUNTY ROAD WORK

Sealed or electronic bids will be received by the Board of Supervisors of Oktibbeha County, Mississippi at the Office of the Chancery Clerk, 101 East Main Street Starkville, Mississippi 39759 until 10:00 A.M. Thursday, May 27th, 2021 for miscellaneous county road and bridge repair at which time they will be publicly opened and read aloud.

Bid A:	Furnish and install soil-cement base stabilization for county roadways in accordance with Section S-308-A and S-308-B of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.  Application rate is 39.71 pounds per square yard for 8 inch incorporation depth over 22 feet roadway width.

Bids shall be based on a rate per mile and shall include all materials and labor necessary to complete the work.

$______________________/ PER MILE

Bid B:	Mill existing asphalt and/or DBST and furnish and install soil-cement base stabilization for county roadways in accordance with Section S-308-A and S-308-B of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.  Application rate is 39.71 pounds per square yard for 8 inch incorporation depth over 22 feet roadway width.

Bids shall be based on a rate per mile and shall include all materials and labor necessary to complete the work.

$______________________/ PER MILE

Bid C:	Removal of existing asphalt pavement on county roadways in accordance with Section S-202 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.

Bids shall be based on a rate per square yard and shall include all materials and labor necessary to complete the work.

$______________________/ PER S.Y.

Bid D:	Furnish and install double bituminous surface treatment for county roadways in accordance with Section S-410 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.  Application rate is 100.0 gallons CRS-2P and 5.68 tons #57 stone per station for Mat Coat and 90.0 gallons CRS-2P and 3.79 tons #7 stone per station for Seal Coat.

Bids shall be based on a rate per mile for a 20 ft. roadway and shall include all materials and labor necessary to complete the work.

$______________________/ PER MILE

Bid E:	Furnish and install hot mix asphalt paving for county roadways in accordance with Section S-403 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.  Material shall be a surface course meeting MDOT specifications for MT-9.5.

Bid is for a 2 in. lift on a 20 ft. roadway and shall include all materials and labor necessary to complete the work.

$______________________/ PER MILE

Bid F:	Furnish and install HP-10x42 piles in accordance with Section S-803 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition. Length = 20 ft.

$______________________/ PER EACH

Bid G:	Furnish and install HP-10x42 piles in accordance with Section S-803 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition. Length = 30 ft.

$______________________/ PER EACH

Bid H:	Furnish and install 4” wide thermoplastic edge stripe (continuous white) (60 mil) in accordance with Section S-621 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.

Bids shall be based on a rate per mile and shall include all materials and labor necessary to complete the work.

$______________________/ PER MILE

Bid I:	Furnish and install 4” wide thermoplastic traffic stripe (skip yellow) (90 mil) in accordance with Section S-621 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.

Bids shall be based on a rate per mile and shall include all materials and labor necessary to complete the work.

$______________________/ PER MILE

Bid J:	Furnish and install 4” wide thermoplastic traffic stripe (continuous yellow) (90 mil) in accordance with Section S-621 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.

Bids shall be based on a rate per linear foot and shall include all materials and labor necessary to complete the work.

$______________________/ PER LINEAR FOOT

Bid K:	Furnish and install thermoplastic legend (white) (120 mil) in accordance with Section S-621 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.

Bids shall be based on a rate per square foot and shall include all materials and labor necessary to complete the work.

$______________________/ PER SQUARE FOOT

Bid L:	Furnish and install 4” wide traffic stripe (continuous white) in accordance with Section S-619 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.

Bids shall be based on a rate per mile and shall include all materials and labor necessary to complete the work.

$______________________/ PER MILE

Bid M:	Furnish and install 4” wide traffic stripe (skip yellow) in accordance with Section S-619 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.

Bids shall be based on a rate per mile and shall include all materials and labor necessary to complete the work.

$______________________/ PER MILE

Bid N:	Furnish and install 4” wide traffic stripe (continuous yellow) in accordance with Section S-619 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.

Bids shall be based on a rate per linear foot and shall include all materials and labor necessary to complete the work.

$______________________/ PER LINEAR FOOT

Bid O:	Furnish and install traffic legend (white) in accordance with Section S-621 of the Standard Specifications for State-Aid Road and Bridge Construction, latest edition.

Bids shall be based on a rate per square foot and shall include all materials and labor necessary to complete the work.

$______________________/ PER SQUARE FOOT

Bid P:	Furnish and deliver quarter inch block material meeting attached specifications.

Bids shall be based on a rate per ton and shall include all materials and labor necessary to complete the work.

$______________________/ PER TON

Proposals shall be good for a period of 180 days from date of signing.

Plan Holders are required to log-in or register for an account to view or order bid documents at www.pritchardengineeringplans.com.  Bid documents are non-refundable and must be purchased through the website. Questions regarding website registration and online orders please contact Plan House at 662-407-0193. For questions related to the contract documents contact the office of Pritchard Engineering, Inc at (662) 324-2205, 100 Miley Road, Starkville, Mississippi 39759. No partial sets of drawings of project manuals will be issued.

Proposal shall be submitted on this form. Bids may be submitted in person, or for those interested, bids can be electronically submitted at www.pritchardengineeringplans.com under the project page. No oral, telegraphic, telephonic, or e-mail proposals will be considered. For sealed bids, the current Certificate of Responsibility Number of the bidder shall appear on the outside of each sealed envelope containing a proposal, said envelope being plainly marked Bid for Oktibbeha County Road and Bridge Repair.  If submitting electronically, please include this information on a cover page with your bid submission.

Each Bid must be accompanied by a bid bond/security deposit or certified check in an amount equal to 5% of the bid, payable to Oktibbeha County as bid security. In the event that an electronic bid is submitted, a copy of the bid bond must be included with the submission. If submitting electronically, a hard copy of all bid documents must be provided within 3 business days if requested after the bid opening.

Joe Williams, President

Oktibbeha County Board of Supervisors

Publish Dates:	April 28 and May 5