COPIAH-LINCOLN COMMUNITY COLLEGE

WESSON, MISSISSIPPI  39191

Specifications:

Lease Fifty (50) Fleet Golf Cars and up to four (4) Multiple Passenger Cars

Request for Bids

Bid No. #744

Bid date:   February 27, 2023

Copiah-Lincoln Community College

Attn:  Erin B. Likens

P.O. Box 649

Wesson, MS.  39191

Bid must be signed and sealed with bidder’s name and address on outside of the envelope, and the time and date of the bid opening and the bid file number shown in the lower-left corner of envelope.

Bids may be hand delivered or sent by mail.  To guarantee delivery by express delivery service we suggest that you mail your bid by UPS or U.S. Postal Service Mail three (3) days prior to the bid opening date.

Any questions, please contact Erin Likens, Purchasing Director, 601-643-8316 or Bradley Boykin 601-643-8779.

Copiah-Lincoln Community College

Bid No. 744

BID Options

Option 1:	Straight Operation Lease

Three (3) Year Term for Fifty (50) Gasoline Golf Cars  		$________ Ea.   $_________

Three (3) Year Term for Four Passenger Gasoline Golf Cars        $________ Ea.   $_________

The college has the ability to lease up to 8 units. The minimum amount will be 2 units.

Option 2:	Operation Lease with a $1,000.00 Balloon

Three (3) Year Term for Fifty (50) Gasoline Golf Cars  		$________ Ea.   $_________

Three (3) Year Term for Four Passenger Gasoline Golf Cars        $________ Ea.    $_________

The college has the ability to lease up to 8 units. The minimum amount will be 2 units.

Option 3:	Lease to Purchase ($1.00 buyout)

Three (3) Year Term for Fifty (50) Gasoline Golf Cars  		$________ Ea.   $_________

Three (3) Year Term for Four Passenger Gasoline Golf Cars        $________ Ea.    $_________

The college has the ability to lease up to 8 units. The minimum amount will be 2 units.

Option 4:	Straight Purchase

Straight Purchase Option 					$________ Ea.   $_________

Three (3) Year Lease for Four Passenger Gasoline Golf Cars        $________ Ea.   $_________

The college has the ability to lease up to 8 units. The minimum amount will be 2 units.

Delivery Schedule:  ______________________________________________________

Bid price to include delivery materials, FOB Wesson campus.

Guarantee:  Each bidder will guarantee the product bid against defect in materials or workmanship for the period of the lease.  The successful bidder further guarantees to replace without cost to Copiah-Lincoln Community College

Comment:  _____________________________________________________________

______________________________________________________________________

Leasing Company:  _________________________________________

Dealer:  __________________________________________________

Dealer Representative:  ______________________________________

Dealer Address:  ___________________________________________

Dealer Telephone:  	__________________   Dealer Fax#:  ______________

Dealer Cell Phone: 	__________________

Leasing Company Representative:  _____________________________

Leasing Company Address:  ___________________________________

Leasing Co. Telephone:  _____________    Leasing Co. Fax#:_____________

Leasing Cell Phone:   _______________

SPECIFICATIONS

FIFTY (50) GASOLINE GOLF CARS

Quantity:  Fifty (50) 2024 Gasoline Powered Fleet Golf Cars & a minimum of Two (2) 4 seat Passenger Gasoline Powered Golf Cars.

Color:  Standard Color Option

Warranty:  All units shall be warranted against defects in material and workmanship

A Brochure of units bidding must be submitted with bid.

Bid price must include delivery to Wesson campus point of delivery Wolf Hollow Golf Club.

Successful Vendor must guarantee delivery between September 17th & September 28th

First payment to be made in October of 2020.

The awarded company will be required to provide at no expense to CLCC, the transportation of the current Yamaha fleet (50 vehicles) from Wolf Hollow Golf Course to Yamaha Golf-Car Company, located in Newnan, Ga.

Please state clearly any incentive offered to Copiah-Lincoln Community College.

Standard fleet model shall have all standard equipment:

- Four (Drink Holders)

2.    	Sun Top/Canopy-UV Stable material with handholds

3.    	Two (2) numbered decals per car & course logo

4.   	Engine:  Minimum 11.4 or better horsepower, 357 CC OHV, 4-cycle,

Single cylinder, Fuel Injected

5.    	Body:  Automotive Style ladder-style steel frame mated to a polypropylene structured floor.

6.    	Drive and Transmission:  automatic torque convertor with

Forward, Neutral and reverse (FNR) axle, ground speed governor.

7.   	Brakes:  self-adjusting mechanical individual rear brakes, hill brake with automatic release

8.    	Steering:  Automotive worm gear style or rack and pinion.

9. 	Bumpers:  Front and rear 5MPH energy absorbing

10.  	Fuel Tank Capacity: - 5.8 gallon tank or better, US unleaded gas only

11. 	Suspension: Fully Independent Automotive Style Strut Suspension on both the front & rear of the vehicle.

12.  	Muffler:  Muffler will be required to be encapsulated for noise reduction.

13.	Sand Bottles (2 per unit)

14.	Fold down windshield & wheel covers & information card holder (1)

15.  	Dual USB Ports.

16.	Tow System

17.	Golf Cart to be the latest model produced by awarded manufacture.

Four (4) Passenger Golf Car model shall have all standard equipment:

1.	Four (Drink Holders)

2.    	80 inch Sun Top/Canopy

3.   	Engine:  Minimum 11.4 or better horsepower, 357 CC OHV, 4-cycle,

Single cylinder, Fuel Injected

4.    	Body:  Automotive Style ladder-style steel frame mated to a polypropylene structured floor.

5.    	Drive and Transmission:  automatic torque convertor with

Forward, Neutral and reverse (FNR) axle, ground speed governor.

6.   	Brakes:  self-adjusting mechanical individual rear brakes, hill brake with automatic release

7.    	Steering:  Automotive worm gear style or rack and pinion.

8. 	Bumpers:  Front 5MPH energy absorbing

9.  	Fuel Tank Capacity: - 5.8 gallon tank or better, US unleaded gas only

10. 	Suspension: Fully Independent Automotive Style Strut Suspension on both the front & rear of the vehicle.

11.  	Muffler:  Muffler will be required to be encapsulated for noise reduction.

12.	Head and Tail Lights

13.	Fold down windshield & wheel covers

14.  	Dual USB Ports.

15.	Rear Facing Seat that converts to a Flat Bed

16.	Golf Cart to be the latest model produced by awarded manufacture.

Service Requirements

- Annual Preventive Service to be included for the awarded fleet after/on the 12th & 24th month of the requested 3-year lease.

- Wolf Hollow to receive a minimum of one (1) service visit per month for the duration of the 36-month lease.

Manufacturer:  ___________________________

Model No./Year Bidding:  _______________________

Demo upon request. Copiah-Lincoln reserves the right to reject any/or all bids.

**Or Equivalent to**