SHELBY SPECIALTY GLOVES

## 5002 & 5002F

Specifications:

### Outer Shell: Heavy 3 to 3.25 oz, popcorn and black color abrasion resistant, multidirectional fiber structure, brushed pigskin. Tanned hide does not contain PCP (pentachlorophenol), it’s salts or esters.

### 4” Nomex wristlet, 5002F No Wristlet

Pattern: Gunn cut, keystone double layer thumb crotch protection.  1/8” wide, double row stitching around inset thumb.

Storage Attachment: Leather, 6mm x 51mm cut length, double stitched 38mm apart

Binding: Black 29mm Cotton (only model 5002F).

Wrist Shirring:  10mm Natural Elastic

Thread:  Lock-Stitch sewn with kevlar thread, 8-10 stitches per inch.  Spun Kevlar thread, tex 70,27.5 to 30.0/4 count, minimum break 12.0#

Origin:      Made in U.S.A.

Meets NFPA 1977, 2011 Edition

# Sizes:             XS, S, M, L, XL, J

Design & Construction:  Anatomically designed gunn cut, keystone glove and thumb pattern.  The glove body shall extend 1” above the wrist crease & shall have shirred elastic snuggler.  Glove shall have bound hem and machine washable.  Meets NFPA 1977,2011 Edition

Shelby Specialty Gloves

3035 Centre Oak Way Suite 102

Germantown, TN. 38138

Phone: 800-888-3598  Fax: 901-362-9127   Email: sales@shelbyglove.com