BID REQUIREMENTS AND SPECIFICATIONS

FOR

WATER METERS

Bid Requirements

The Jackson County Utility Authority is accepting sealed bids for water meters.

Bids will be accepted until 10:00 a.m. on June 25, 2018, then opened and read aloud shortly thereafter.

Bids must be in a sealed envelope addressed to the Jackson County Utility Authority, 1225 Jackson Avenue, Pascagoula, MS 39567, and must be clearly marked on the outside of the envelope:

“WATER METER BID - DO NOT OPEN”

Bids may also be submitted electronically at www.centralbidding.com.  For any questions relating to the electronic bidding process, please call Central Bidding at 225-810-4814,

Delivery is the sole responsibility of the bidder.  The Authority is not responsible for lost, misdirected, or late mail.

Submission of a bid proposal constitutes agreement on the part of the Bidder to all aspects of the requirements and specifications of this document.

All bids must be submitted on the attached bid form, and must be signed and dated.  Bid shall include a manufacturer’s material specification for material being submitted for bid.  Bidder shall enter the delivery time to the nearest whole day.  Delivery time shall be defined as the time required (in calendar days) to deliver the requested material to the Authority from the date the request for material is sent to the Supplier.

It is the intent of the Authority to award the bid to the bidder providing the lowest and best bid. Delivery time is weighted heavily in the selection of best bid.

The Authority reserves the right to reject any and/or all bids received.

It shall be incumbent upon the bidders to understand the specifications.  Requests for clarifications shall be in writing and shall be submitted to the Authority at least five (5) days prior to the time and date set for the bid opening.  The specifications and conditions of this bid are intended to promote competition to the maximum extent practicable.  It is the responsibility of the bidder to notify the Authority’s Purchasing Agent of restrictive competition.  The notice of restrictive specifications/conditions must be submitted to the Authority at least five (5) days prior to the bid opening.  Failure to conform to this requirement may be cause for a protest to be rejected.

The Authority intends to enter into a contract for the purchase of water meters for two (1) year, with an option to renew for (2) two  one (1) year periods..  The bid prices shall remain in effect for the for duration of contract.

Bid shall include all costs associated with the purchasing of the water meters including delivery cost.

Specification sheets shall be provided with your bid, if bidding other than requirements set forth in water meter standard specifications.

The vendor shall invoice the Authority for each of the separate deliveries and reference the purchase order number assigned.  Invoice shall reflect the bid price for the each unit and the total amount of each delivery.  No additional amount will be paid by the Authority.

All deliveries shall be FOB Jackson County Utility Authority, 11028 HWY  57, Vancleave, MS, 39565 between the hours of 8:00 a.m. and 3:00 p.m., Monday through Friday.  Two business day’s notice is required for deliveries. The Supplier shall provide equipment and personnel necessary to handle the materials and remove them from the delivery truck using methods recommended by the material manufacturer to prevent damage to the materials or surrounding surfaces. No delivery shall be removed from the truck prior to authorized personnel reviewing the delivery ticket and accepting the condition and quantity of the materials for delivery.

If the successful Bidder fails to provide required units or fails to correct problems within fifteen (15) days of notification by the Authority of such problems, the Jackson County Utility Authority reserves the right to cancel the proposed contract with thirty (30) days written notification by the Authority to the Bidder.

In the event the successful bidder fails to provide commodities contained in his bid for reasons beyond his control, purchases of such commodities shall be made by the Authority from one (1) of the bidders whose bid was accepted as an alternate.

The successful bidder shall provide written response with delivery date of requested materials to the Authority within 2 business days of the request of materials.  Failure to respond to the request shall signify the successful bidder cannot deliver the materials and the Authority will request materials from an alternate bidder.

Questions may be directed to Richard Torjusen in the Authority’s Purchasing office by calling 228-938-6809, ext. 5337.

GENERAL WATER METER SPECIFICATIONS

The meters shall be compatible with an existing Neptune Metering and Reading System.

1.	Type: Automatic Remote Read for installation in pit or below ground vault and shall be tamper-proof and sealed for moisture protection.

2.	Units of Measurement: U.S. Gallons and Cubic Feet

3.	Available Sizes: 5/8”x 3/4”, 1”, 1 ½”, and 2”

4.	Operating Temperature: -22 degrees F to 149 degrees F

5.         Battery Life and Warranty: 20 years (minimum) with 10 years non-pro-rated.                     Battery shall be field replaceable and protected from water, dust, and chemicals.

6.         Communication: Via RF on an unlicensed bandwidth.

7.         Meter shall provide tamper, leak, reverse flow detection, and a minimum of one                            month of rolling memory.

8.         Shall not require any external wiring outside of the meter unit nor a through the 		            lid antenna.

9.         Manufacturer: Neptune Model T-10 w/R900i transmitter and/or equal.  An                        alternate or equal submittal must be readable by Neptune’s software                                   system without upgrades or replacement.

BID FORM

TO:	JACKSON COUNTY UTILITY AUTHORITY

1225 JACKSON AVENUE

PASCAGOULA, MS 39567

BIDDER:         ___________________________________________________________

ADDRESS:      ___________________________________________________________

___________________________________________________________

TELEPHONE: ____________________________

DATE: ___________________________________

Delivery Time							Price

______________        	WATER METERS – 3/4"	  $   ____________

______________            	 WATER METERS – 1”	  $   ____________

______________		WATER METERS – 1-1/2”	   $   ____________

_______________		WATER METERS – 2”	  $    ____________

BIDDER’S SIGNATURE: __________________________________________

BIDDER’S NAME (Type or Print): ___________________________________