# REQUEST FOR PROPOSALS

TO PERFORM EARTH WORK IN THE FORMATION

AND CONSTRUCTION OF A NEW 4.2 ACRE CELL

LOCATED AT THE MONROE COUNTY LANDFILL,

MONROE COUNTY, MISSISSIPPI

____________________________________________________________________________

# INTRODUCTION AND GENERAL TERMS

Monroe County, Mississippi has experienced damages due to a tornado event occurring on March 24, 2023, resulting in the loss of life, personal injuries, and substantial damages to both improved and unimproved property.  The vegetation and other debris resulting from this devastating tornado has prompted the need to immediately expand the capacity at the Monroe County Sanitary Landfill, (hereinafter “Monroe County Landfill”), on an emergency basis.  Accordingly, the Board of Supervisors of Monroe County, Mississippi, (hereinafter “Board”), is seeking a qualified Contractor (hereinafter “Contractor”), to perform the scope of work addressed in this emergency Request for Proposals (hereinafter “RFP”).  All proposals must be properly certified by the entity bidding for the work and signed by an officer, director, or owner that has authority to bind and commit the Contractor to perform said work and services.  Contractors desiring to perform and provide the services, described in the Scope of Work, shall submit sealed proposals in an original and four (4) complete copies not later than 9:00 a.m. CDT, April 28, 2023, to the Board of Supervisors of Monroe County, MS, at the Monroe County Chancery Courthouse, 201 W. Commerce Street, Aberdeen, MS 39730.  Unless modified in writing by the Board, as set forth herein, a submitted proposal shall remain in full force and effect until the proposal is either rejected by the Board or, if accepted and awarded, until the contract work is fully completed with a certificate of completion being executed therewith.

Email submissions will be acceptable.  However, offers by telephone, fax or telegram will not be acceptable.

Contractor proposers, (hereinafter “proposers”), are cautioned that they are responsible for the delivery of their proposal to the specific location cited above. Therefore, if the proposal is delivered by an express mail carrier or by any other means, it is the proposer’s responsibility to ensure delivery to the above address.  This Board will not be responsible for deliveries made to any place other than the specified address.

It is the sole responsibility of the proposer to ensure that his or her proposal timely reaches the Board. The time and date for receipt of proposals will be scrupulously observed.  Late deliveries or mail delays will be rejected as non-responsive regardless of the reason for delay. The Board will meet at 9:00 o’clock a.m., CDT, on the 28th day of April, 2023, to receive, grade, and award the contract to the successful proposer.  The Board may elect to interview proposers prior to the 9:00 a.m. meeting time. All costs of preparation of a response to this request for proposals are solely those of the proposers.  The Board assumes no responsibility whatsoever for any such costs incurred by a proposer. The proposer also agrees that the Board bears no responsibility for any costs associated with any administrative or judicial proceedings resulting from the solicitation process. The Board reserves the right to accept or reject any or all proposals, with or without cause, to waive technicalities, or to accept the proposal which, in its sole judgment, best serves the interest of Monroe County, or to award a contract to the next most qualified proposer if a successful proposer does not execute a contract within 24 hours after approval of the selection by the Board. The Board reserves the right, to cancel this solicitation at any time prior to approval of the award by the Board. The Board reserves the right to request clarification of information submitted and to request additional information from any or all proposers.

# SCOPE OF WORK

TO PERFORM EARTH WORK IN THE FORMATION

AND CONSTRUCTION OF A NEW 4.2 ACRE CELL

LOCATED AT THE MONROE COUNTY LANDFILL

# 1.0	GENERAL

One or more tornados struck Monroe County, Mississippi, during the evening hours of March 24, 2023, causing loss of life, personal injuries, as well as, substantial damages  to both improved and unimproved property.

The Board of Supervisors of Monroe County, Mississippi, (hereinafter “Board”), in response to said tornado damages declared a state of emergency in Monroe County effective March 25, 2023, which was thereafter followed by a Proclamation, issued by the Governor of the State of Mississippi, pursuant to the authority conveyed in Section 33-15-11(b)(17), Miss. Code Ann., proclaiming a state of emergency in the areas affected by the aforesaid storms.

In order to assist in the remediation of the damages caused by the aforesaid tornado, the Board determined that it would be in the best interest of the citizens of Monroe County to employ contractors to remove and dispose of the storm debris, as well as, to employ a contractor to monitor the debris removal process.   Recognizing the substantial quantity of the storm debris, the Board determined that it was critical to expand the area of the Monroe County Landfill by developing and constructing a new 4.2 acre cell so that the unanticipated debris could be accepted and processed.

# 2.0 	NARRATIVE DESCRIPTION OF THE SERVICES TO BE PROVIDED

Cook Coggin Engineers, Inc., (hereinafter “Cook Coggin”), an engineering firm that is contractually employed by Monroe County, provided advice on the utilization of a geosynthetic clay liner, (“GC Liner”), as opposed to a clay soil surface because an appropriate clay soil was not available at an affordable price, primarily because of the substantial transportation costs; the 4.2 acre cell will be constructed in a rectangular shape abutting an existing cell located immediately north of the 4.2 acre call, as depicted on a topographical survey  of the cell which was prepared by Cook Coggin.

The construction plan is described as follows, to wit:

The subgrade will consist of firm soils, free of organic matter and rocks, that will provide a stable base on which the GC Liner will be placed.  A 2 foot wide by 2 foot deep anchor trench for the GC Liner will be dug on three of the borders of the cell, excepting the border that is adjacent to the existing cell to the north.  Likewise, a 2 foot high earthen berm will be constructed around the same three perimeter sides of the cell, again excepting the perimeter side on the northern boundary of the 4.2 acre cell.  This will secure the GC Liner.  Where the cell adjoins the adjacent existing cell, the GC Liner will be placed directly on the surface of the existing cell slope.  The installation of the GC Liner will be undertaken pursuant to a separate contract with Environmental Specialties International, Inc.  Subsequent to the placing of the GC Liner, an upper protective soil layer will be laid, which will protect the GC Liner from equipment operations and waste debris.  The thickness of the protective soil layer is to be 2 feet and will be surveyed to document the final thickness.  The preliminary estimate for the quantity of dirt for the construction of the berm and the protective covering of the GC Liner ranges between 13,000 to 16,000 cubic yards.  The excavated dirt from the perimeter trenches, any dirt that is made available through the final preparation of the subgrade, and other dirt available at the landfill site, can be used to meet the aforesaid estimated quantity.  The earth work and the construction related thereto will be included in a separate contract from the acquisition and placing of the GC Liner.

Environmental Specialties International, Inc., (hereinafter “ESI”), is a certified installer of geosynthetic materials for various manufacturers and has completed numerous projects similar to the proposed construction of the additional cell at the Monroe County Landfill; ESI will provide all supervision, labor, equipment, and materials necessary for the completion of the geosynthetic liner component of the Landfill project.

3.0	OTHER SOURCES OF INFORMATION THAT DESCRIBE THE SOURCE OF WORK APPLICABLE TO THE EARTH WORK FORMATION AND CONSTRUCTION OF THE 4.2 ACRE CELL AT THE MONROE COUNTY LANDFILL

A topographical survey of the 4.2 acre cell, prepared by Cook Coggin Engineers, Inc., will be made available at the Office of the Monroe County Chancery  Clerk, 201 W. Commerce St., Aberdeen, MS 39730, or at the offices of Cook Coggin Engineers, Inc., 703 Crossover Rd., Tupelo, MS  38801.

Specifications for the project, including the project specific Mississippi Department of Environmental Quality (MDEQ) approved Construction Quality Assurance/Quality (CQA/CQC) Plan, prepared by James (Jimmy) R. Spencer, RPG, Geologist/ Environmental Coordinator, Cook Coggin Engineers, Inc., will be made available by Mr. Spencer at Cook Coggin Engineers, Inc., 703 Crossover Rd., Tupelo, MS  38801; telephone:  (662) 842-7381.

Other informational contacts are identified as follows:

Tony Ligon, Manager, Monroe County Landfill:	(662) 305-2898 (c)

(662) 369-6654 (o)

tligon@monroems.com

Daniel Williams, Manager, Monroe County

Road Department:					(662) 304-0019 (c)

dwilliams@monroems.com

A description of the GC Liner installation process, developed by Environmental Specialties International, Inc., will be made available pursuant to request.

4.0	PERFORMANCE

4.1	Because of the emergency circumstances that exist related to the need for available space at the Monroe County Landfill to accommodate the unanticipated storm debris, time is of the essence in the performance of this project and the work of the Contractor.

4.2	The Contractor must be prepared to coordinate the performance of the timing of the earth work with the installation of the GC Liner by Environmental Specialties International, Inc.  As can be seen from the narrative of the scope of the project work, there must be earth work timely performed prior to the installation of the GC Liner, as well as, during and after the installation of the liner.  The earth work Contractor shall be on site on each day that the GC Liner is installed to cover and protect each section of the liner.  The Contractor shall be liable to the County or to Environmental Specialties International, Inc., should it negligently damage the liner during its daily operations to cover and protect the liner.

4.3	Because of the time sensitivity, the Contractor must be mobilized and prepared to commence work at the project site no later than 72 hours following being notified that it has been awarded the contract work.  The entire time of the contract period shall be a total of two weeks from the date of commencement.

5.0	APPLICABLE LAWS, REGULATIONS, AND OTHER CONSIDERATIONS.

5.1	The Contractor shall supervise and direct the work, using a skillful labor and proper equipment for all tasks. Safety of the Contractor’s personnel and equipment is the responsibility of the Contractor. Additionally, the Contractor shall pay for all materials, personnel, taxes, and fees necessary to perform under the terms of this contract.

5.2	The Contractor shall be duly licensed and permitted in accordance with state and county statutory requirements to perform the project work.

5.3	The Contractor shall be responsible for taking corrective action in response to any notices of violations issued as a result of the Contractors’ or any subcontractors’ actions or operations during the performance of this contract. Corrections for any such violations shall be at no additional costs to the County.

5.4	The Contactor shall be responsible for control of pedestrian and vehicular traffic in the work area. The Contractor shall provide all flag persons, signs, equipment, and other devices necessary to meet federal, state, and local requirements. The traffic control personnel and equipment shall be in addition to the personnel and equipment required in other parts of this contract. At a minimum, one flag person should be posted at each approach to the work area. Work shall be accomplished in a safe manner in accordance with OSHA standards.

5.5	The Contractor is responsible for obtaining all applicable environmental and regulatory permits prior to the Contractor commencing operations.

5.6	The Contractor is responsible for dust control. The Contractor shall be in compliance with all state and local laws for dust control.

5.7	The County may suspend Contractor operations due to inclement weather. The performance period may be extended for weather delays.

5.8	The Contractor shall employ as many local residents and subcontractors as possible as part of this contract.

5.9	The Contractor shall comply with Executive Order 11246 of September 24, 1965, entitled “Equal Employment Opportunity,” as amended by Executive Order 11375 of October 13, 1967, and as supplemented in Department of Labor regulations (41 CFR chapter 60).

5.10	The Contractor shall comply with the Copeland “Anti-Kickback” Act (18 U.S.C. 874) as supplemented in Department of Labor regulations (29 CFR Part 3).

5.11	The Contractor shall comply with the Davis-Bacon Act (40 U.S.C. 276a to 276a-7) as supplemented by Department of Labor regulations (29 CFR part 5) in so far as it may apply to this contract.

5.12	The Contractor shall comply with Section 103 and 107 of the Contract Work Hours and Safety Standards Act (40 U.S.C. 327 – 330) as supplemented by Department of Labor regulations (29 CFR Part 5).

5.13	The Contractor shall permit access by the County and the government agencies including  the Comptroller General of the United States, or any of their duly authorized representatives to any books, documents, papers, and records of the Contractor which are directly pertinent to that specific contract for the purpose of making audit, examination, excerpts, and transcriptions.

5.14	The Contractor shall retain all required records for three years after the County or the relevant government agencies make final payments and all other pending mattes are closed.

5.15	Compliance with all applicable standards, orders, or requirements issued under section 306 of the Clean Air Act (42 U.S.C. 1857(h)), Section 508 of the Clean Water Act (33 U.S.C. 1368), Executive Order 11738, and Environmental Protection Agency regulations (40 CFR part 15).

5.16	The Contractor shall agree to comply with any other applicable federal, state or local regulations.

5.17	The Contractor shall adhere to mandatory standards and policies on energy efficiency which are contained in the state energy conservation plan issued in 	compliance with the Energy Policy and Conservation Act (42 U.S.C. 6201).

5.18	Contractor shall not subcontract with any parties listed on the government wide Excluded Parties List System in the System for Award Management (SAM), in accordance with the OMB guidelines at 2 CFR 180 that implement Executive Orders 12549 (3 CFR Part 1986 Comp., p. 189) and 12689 (3 CFR Part 1989 Comp., p. 235), “Debarment and Suspension.”

5.19	Contractor shall certifies that it will not and has not used federal appropriated funds to pay any person or organization for influencing or attempting to influence an officer or employee of any agency, a member of Congress, officer or employee of Congress, or an employee of a member of Congress in connection with obtaining any Federal contract, grant or any other award covered by 31 U.S. C. 1352. Contract shall also disclose any lobbying with non-federal funds that takes place in connection with obtaining any federal award. Contractor shall require all subcontractors to submit these same certifications.

5.20	Contractor shall comply with section 6002 of the Solid Waste Disposal Act, as amended by the Resource Conservation and Recovery Act. The requirements of Section 6002 include procuring only items 	designated in guidelines of the Environmental Protection Agency (EPA) at 40 CFR Part 247 that contain the highest percentage of recovered material practicable, consistent with maintaining a satisfactory level of competition, where the purchase price of the item exceeds $10,000 or the value of the quantity acquired by the preceding fiscal year exceeded $10,000; procuring solid waste management services in a manner that maximizes energy and resource recovery; and establishing an affirmative procurement program for procurement of recovered materials identified in the EPA guidelines.

6.0	BONDING AND INSURANCE.

6.1	Prior to signing of contract, Contractor agrees to furnish the County with all applicable certificates of insurance. A bid bond in the amount of $25,000 shall accompany the proposal. In addition, payment and performance bonds with each being equal to the bid or $250,000.00, whichever is higher, are required within 24 hours of award of the contract. The Contractor shall be able to cover expenses associated with a major recovery operation prior to the initial payment and between subsequent payments, as well as, the aforementioned bonds and insurance. Contractor mobilization costs will not be paid if the Contractor is unable to obtain bonding.

6.2	The Contractor shall save and hold the County harmless from and against all liability, claims and demands on account of personal injuries (including without limitation workers’ compensation and death claims) or property loss or damages of any kind whatsoever, which arise out of or be in any manner connected with, or are claimed to arise out of or be in any manner connected with, the performance of this contract, regardless of whether such injury, loss or damage shall be caused by, or be claimed to be caused by, the negligence or other fault of the Contractor, any subcontractor, agent or employee.

6.3	Within 24 hours following signing of contract, Contractor shall provide copies of insurance policies including all endorsements.

•	Commercial General Liability – in the amount of three million dollars ($3,000,000.00) aggregate/five hundred thousand dollars ($500,000.00) per occurrence. The General Aggregate limit shall either apply separately to the resulting Contractor or shall be at least twice the required occurrence limit.

•	Comprehensive Automobile Vehicle Liability – covering any automotive equipment to be sued in performance of the service, with a minimum limit in the amount of five hundred thousand dollars ($500,000.00) per occurrence combined single limit / any auto. Physical Damage Insurance covering owned or rented machinery, tools, equipment, office trailers, and vehicles.

•	Worker’s Compensation – Proposer shall provide a policy with employer’s liability coverage with limits of not less than One Million Dollars ($1,000,000.00) per occurrence for each accident or illness. The Worker’s Compensation policy shall state that it cannot be cancelled or materially changed without first giving thirty (30) days prior notice thereof in writing to the County. Firms that have owner/operators that have filed a “Notice of Election to be Exempt” shall supply a signed copy of said notice. Any such exemption shall meet the requirements that qualify for an exemption under the applicable Worker’s Compensation law.

•	Contractor agrees that the insurer shall waive it rights of subrogation, if any, against the County on Commercial General Liability and Worker’s Compensation insurance coverage. The ACORD Certificate of Liability Insurance, with endorsements, shall be completed by the authorized Agent and returned to the County.

•	Loss Deductible Clause:  The County shall be exempt from, and in no way liable for, any sums of money that may represent a deductible in any insurance policy. The payment of such deductible shall be the sole responsibility of the Contractor.

•	The Contractor shall promptly remedy damage and loss to property caused in whole or in part by the Contractor, its subcontractors of every tier, anyone directly or indirectly employed by any of them, or anyone for whose acts they may be liable.

•	Conditions:  Each insurance policy shall include the following conditions by endorsement to the policy:

º	Each policy shall require that thirty (30) days prior to expiration, cancellation, nonrenewal or any material change in coverage’s or limits, a notice thereof shall be given to the County by a certified mail. Contractor. shall also notify the County, in a like manner, within twenty-four (24) hours after receipt, of any notices of expiration, cancellation, non-renewal, or material change in coverage received by said Contractor from its insurer, and nothing contained herein shall absolve the Contractor of this requirement to provide notice.

º	Companies issuing the insurance policy, or policies, shall have no recourse against the County for payment of premiums.

The term “Owner” and/or “County” shall include all Authorities, Boards, Bureaus, Commissions, Division, Departments and Offices of the County and individual members, elected officials, employees thereof in their official capacities, and/or while acting on behalf of the County.

County shall be named as an additionally insured on all policies of insurance. The policy clause “Other insurance” shall not apply to any insurance coverage currently held by the County to any future coverage, or to the County’s Self Insured Retentions as, if any of whatever nature.

7.0 	PAYMENT.

7.1	Time is of the essence to the performance hereunder and the County shall recover from the Contractor any delay costs caused by the acts or omissions of the Contractor or its agents. Except as otherwise provided herein, payment shall be made for actual work accepted and completed. No late payment interest shall be due and owing for payments withheld in good faith for reasonable cause.  Because this contract is of short duration, final payment will be made following completion of the contract work.

7.2 	The County may withhold payment or final payment for reasons including, but not limited to the following: unsatisfactory job performance or progress, defective work, disputed work, failure to comply with material provisions of the contract, third party claims filed or reasonable evidence that a claim will be filed or other reasonable cause.

7.3	Final payment, less any offsets or deductions authorized hereunder or by law, shall be made within thirty days of the certification of completion of the project by the County’s authorized agent provided the Contractor has completed filing of all contractually required documents and certifications with the County’s authorized agent including acceptable evidence of the satisfaction of all claims or liens.

8.0	CHANGES, ADDITIONS, DEDUCTIONS AND EXTRA WORK

Upon proper action by the County the County’s authorized agent may authorize changes, additions or deductions from the work to be performed by written notice to the Contractor.  No extra work shall be done or any obligation incurred except upon written order by the County’s authorized agent.  If any change causes an increase or decrease in the Contractor’s cost of, or the time required for, the performance of any part of the work, under this contract, the County’s authorized agent shall make an equitable adjustment and modify the contract in writing.

9.0	TERMINATION OF THE CONTRACT

9.1	This contract may be terminated at any time for the convenience of the County. The 	County agrees to pay the contractor for all work completed through the termination date, 	as well as, any demobilization costs that were a part of the original contract.

9.2     This contract shall be terminated for cause if the Contractor defaults in the performance of any of the terms hereof, including but not limited to:  unsatisfactory job performance or progress, defective work, disputed work, failure to comply with material provisions of the contract, third party claims filed or reasonable evidence that a claim will be filed, or other reasonable cause; or otherwise  if the Contractor fails to cure any other deficiency identified by the County’s authorized agent within 24 hours of delivery of notice of said deficiency.  The County retains all other legal or equitable rights or remedies existing as a result of said default, including but not limited to, any legal process necessary to obtain relief against any sureties securing this contract. Any reasonable attorney’s fee incurred by the County in enforcing this contract will not exceed 15% of said contract price. Jurisdiction for all legal proceedings shall be the courts of Monroe County, Mississippi.

10.0	WARRANTIES AND REPRESENTATIONS

10.1	This contract is binding upon and insures to the benefit of the County or its assigns and is 	the whole agreement of the parties and governed by the Law of the State of Mississippi.

10.2	The Contractor shall comply with all federal, state, and local laws, ordinances, and 	regulations.  The Contractor shall not discriminate against any employee or applicant due 	to sex, race, color, creed, national origin or ancestry.  The Contractor further certifies he 	is eligible to perform this contract under local and federal law, is not now and has never 	been debarred from performing federal or state government contracts, and that all 	subcontractors used in the performance of this contract have the same qualification.

11.0	DEFICIENCIES, CORRECTIVE ACTIONS AND DEDUCTIONS

11.1	When the Contractor’s work does not conform to the Contract requirements completely, a 	deficiency exists.  If a deficiency(s) is serious enough to render a service unacceptable, it 	is also considered a defect.  Defects are important in determining if non-compliance 	levels have been exceeded for services inspected.

11.2	Corrective Actions.  If deficiencies are identified, the County must take action to correct 	these deficiencies using one, or in some cases a combination of, the following:

Stop unsafe work.  The County’s authorized agent may immediately stop work on that 	portion of the job affected by a safety hazard, until it is corrected.

Issue a Stop Work Order.  If the County’s authorized agent determines the deficiency is 	serious, the County can issue a stop work order.

Reduced Value Deduction.  The County may reduce the contract price to reflect the 	reduced value of the services performed.  This method is normally used when the work is 	performed by the County or another contractor rather than the Contractor under this 	contract.  The amount of the deduction is equal to the value of the service(s) not 	performed.  As appropriate, calculation of deductions for certain deficiencies will be 	made using approved methods included in the Contract provision entitled “Inspection of 	Services.”

The Contract may be terminated.

11.3	The County may discuss corrective actions with the Contractor to prevent future 	occurrences.

11.4	The County’s authorized agent will notify the Contractor, in writing, of any observed 	noncompliance with the aforementioned federal, state, or local laws or regulations. Such 	notice, when delivered to the Contractor at the site of the work, shall be deemed 	sufficient for the purpose. After receipt of such notice, the Contractor shall immediately 	inform the County’s authorized agent of proposed corrective action, and take such action 	as may be approved. If the Contractor fails or refuses to comply promptly, the County's 	authorized agent may issue an order stopping all or part of the work until satisfactory 	corrective action has been taken. No part of the time lost due to any such stop orders shall 	be made the subject of a claim for extension of time, or for excess costs or damages by 	the Contractor.

12.0	NOTICES

12.1	At the time of the award, the Contractor shall designate, in writing, a Contractor’s 	Representative (CR) to receive any notice required hereunder and who shall be available 	at the local work site in the County, during all times that the Contractor is performing 	work in accordance herewith. A copy of said designation shall be provided to the 	County’s authorized agent at the time of award.

12.2	The County individual authorized to receive any notice required hereunder shall be the County’s authorized representative.  Said notice must be hand delivered during normal business hours to County’s authorized representative.

13.0	OTHER CONTRACTS

The County reserves the right to issue other contracts or direct other contractors to 	work within the area included in this contract.

14.0	ATTACHMENTS

1.	Debarment Certification Form

2.	E-Verify Certification Form

15.0	PROPOSAL EVALUATION CRITERIA

Below are the criteria that will be used by the Board to evaluate and score responsive and qualified proposals. Proposers shall include sufficient information to allow the Board to thoroughly evaluate and score their proposals. Each proposal submitted shall be evaluated and ranked by an evaluation committee. The contract will be awarded to the most qualified proposer, per the following:

| CRITERIA |  | WEIGHTED % |
| --- | --- | --- |
| Contractor’s Experience / Past Performance / Individual Credentials of Contractor and Team |  | 30 |
| Proposal/Work Plan for Monroe County Project |  | 30 |
| Price |  | 40 |
| Total Score |  | 100% |

This is solely to allow the selection committee a way to award points for evaluation.

16.0	ACCEPTANCE OF CONTRACT

The Contractor shall provide all the documentation required by specified time limit, as well as, provide a list of all Sub-Contracts and Proof of Insurance of all Sub-Contractors being used under this contract.

Upon motion duly made, seconded and carried, this Request for Proposals for Tornado Debris Removal and Disposal Services was approved by the Board of Supervisors of Monroe County, Mississippi, as and for the act and deed of Monroe County, Mississippi, on the 21st day of April, 2023.

MONROE COUNTY, MISSISSIPPI

___________________________________

HOSEA BOGAN, President,

Monroe County Board of Supervisors

ATTEST:

________________________________

RONNIE BOOZER, Monroe County Chancery Clerk

and Clerk to the Board of Supervisors

ATTACHMENT 2

LIST OF PROPOSED SUBCONTRACTORS

DISASTER DEBRIS REMOVAL AND DISPOSAL

Company Name:								MBE/DBE:

Company Address:

Company Contact Person:

Proposed Scope of Work:

Company Name:								MBE/DBE:

Company Address:

Company Contact Person:

Proposed Scope of Work:

Company Name:								MBE/DBE:

Company Address:

Company Contact Person:

Proposed Scope of Work:

Company Name:								MBE/DBE:

Company Address:

Company Contact Person:

Proposed Scope of Work:

(Make Additional Copies of this Sheet if Needed)

ATTACHMENT 1

REQUEST FOR PROPOSAL

CERTIFICATION REGARDING DEBARMENT,

SUSPENSION AND OTHER RESPONSIBILITY MATTERS

CERTIFICATION REGARDING DEBARMENT, SUSPENSION, AND OTHER RESPONSIBILITY MATTERS -Certification in accordance with Section 29.510 Appendix A, C.F.R./Vol. 53, No. 102, page 19210 and 19211:

(1)	The CONTRACTOR certifies to the best of its knowledge and belief that it and its principals:

(a) 	are not presently debarred, suspended, proposed for debarment, declared ineligible, or voluntarily excluded from covered transactions by any federal department or agency;

(b) 	have not within a three-year period preceding this proposal been convicted of or had a civil judgment rendered against them for commission of fraud or a criminal offense in connection with obtaining, attempting to obtain, or performing a public (federal, state or local) transaction or contract under a public transaction, violation of federal or state antitrust statutes or commission of embezzlement, theft, forgery, bribery, falsification or destruction of records, making false statements, or receiving stolen property;

(c)	are not presently indicted for or otherwise criminally or civilly charged by a governmental entity (federal, state or local) with commission of any of the offenses enumerated in paragraph (l)(b) of this certification: and

(d)	have not within a three-year period preceding this application/proposal had one or more public transactions (federal, state or local) terminated for cause or default;

(e)	has not either directly or indirectly entered into any agreement participated in any collusion; or otherwise taken any action in restraint of free competitive negotiation in connection with this CONTRACT.

(2)	The CONTRACTOR further certifies, to the best of his/her knowledge and belief, that:

(f)	No federal appropriated funds have been paid or will be paid to any person for influencing or attempting to influence an officer or employee of any Federal agency, a member of Congress, an officer or employee of Congress, or employee of a member of Congress in connection with the awarding of any Federal loan, the entering into of any cooperative agreement, and the extension, continuation, renewal, amendment, or modification of any Federal contract, grant, loan, or cooperative agreement.

(g)	If any funds other than Federal appropriated funds have been paid or will be paid to any person for influencing or attempting to influence an officer of employee of Congress, or any employee of a member of Congress in connection with this CONTRACT, Standard Form-LLL, "Disclosure Form to Report Lobbying", in accordance with its instructions will be completed and submitted.

The certification contained in (1) and (2) above is a material representation of fact upon which reliance is placed and a pre-requisite imposed by Section 1352, Title 31, U. S. Code prior to entering into this CONTRACT. Failure to comply shall be subject to a civil penalty of not less than $10,000 and not more than $100,000. The CONTRACTOR shall include the language of the certification in all subcontracts exceeding $100,000 and all sub-contractors shall certify and disclose accordingly.

I hereby certify that I am the duly authorized representative of the CONTRACTOR for purposes of making this certification, and that neither I, nor any principal, officer, shareholder or employee of the above firm has:

(a) 	employed or retained for commission, percentages, brokerage, contingent fee, or other consideration, any firm or person (other than a bona fide employee working solely for me or the above CONTRACTOR) to solicit or secure this agreement,

(b) 	agreed, as an express or implied condition for obtaining this CONTRACT, to employ or retain the services of any firm or person in connection with carrying out the agreement, or

(c)	paid, or agreed to pay, to any firm, organization or person (other than a bone fide employee working solely for me or the above CONTRACTOR) any fee, contribution, donation, or consideration of any kind for, or in connection with, procuring or carrying out the agreement; except as herein expressly stated (if any).

I acknowledge that this Agreement may be furnished to the Federal Emergency Management Agency, in connection with the Agreement involving participation of federal disaster relief funds, and is subject to applicable state and federal laws, both criminal and civil.

SO CERTIFIED this day of ____________ , 20___.

CONTRACTOR NAME HERE

BY: ________________________________

{typed name}

ATTEST:________________	__

My Commission Expires: ______________________________________________

Notary

ATTACHMENT 2

REQUEST FOR PROPOSAL

PRIME CONSULTANT / CONTRACTOR EEV CERTIFICATION AND AGREEMENT

By executing this Certification and Agreement, the undersigned verifies its compliance with the, "Mississippi Employment Protection Act," Section 71-11-3 of the Mississippi Code of 1972, as amended, and any rules or regulations promulgated by the CITY, MEMA, Department of Employment Security, State Tax Commission, Secretary of State, Department of Human Services in accordance with the Mississippi Administrative Procedures Law (Section 25-43-1 et seq., Mississippi Code of 1972, as amended), stating affirmatively that the individual, firm, or corporation which is contracting with the BOARD has registered with and is participating in a federal work authorization program* operated by the United States Department of Homeland Security to electronically verify information of newly hired employees pursuant to the Immigration Reform and Control Act of 1986, Pub.L. 99-603,100 Stat 3359, as amended. The undersigned agrees to inform the BOARD if the undersigned is no longer registered or participating in the program.

The undersigned agrees that, should it employ or contract with any entity(s) in connection with the performance of this CONTRACT, the undersigned will secure from such entity(s) verification of compliance with the Mississippi Employment Protection Act. The undersigned further agrees to maintain records of such compliance and provide a copy of each such verification to the BOARD, if requested, for the benefit of the BOARD or this CONTRACT.

_____________________________________________

EEV* Company Identification Number [Required]

The undersigned certifies that the above information is complete, true and correct to the best of my knowledge and belief. The undersigned acknowledges that any violation may be subject to the cancellation of the contract, ineligibility for any state or public contract for up to three (3) years, the loss of any license, permit, certificate or other document granted by any agency, department or government entity for the right to do business in Mississippi for up to one (1) year, or both, any and all additional costs incurred because of the contract cancellation or the loss of any license or permit, and may be subject to additional felony prosecution for knowingly or recklessly accepting employment for compensation from an unauthorized alien as defined by 8 U.S.C §1324a(h)(3), said action punishable by imprisonment for not less than one (1) year nor more than five (5) years, a fine of not less than One Thousand Dollars ($1,000.00) nor more than Ten Thousand Dollars ($10,000.00), or both, in addition to such prosecution and penalties as provided by Federal law.

BY:

Authorized Officer or Agent 						Date

Printed Name of Authorized Officer or Agent 				Title

SWORN TO AND SUBSCRIBED before me on this the _____ day of ____________________, 20____.

__________________________________________

NOTARY PUBLIC

My Commission Expires: ___________________

* 	As of the effective date of the Mississippi Employment Protection Act, the applicable federal work authorization program is E-Verify™ operated by the U. S. Citizenship and Immigration Services of the U.S. Department of Homeland Security, in conjunction with the Social Security Administration.