## Self-Propelled Power Broom

Self-Propelled Power Broom, new and of current model, equipped as advertised by the manufacturer, to meet or exceed the following MINIMUM specifications:

Power Broom Proposed:  Make: ________________________	Model: ________________________

Non-Restrictive

Clause:		Any use of brand name or equal within this specification is to be considered a reference for the purpose of describing the standard of quality, performance, and characteristics desired.  It is not intended to limit or restrict competition.

# SPECIFICATIONS

Operating

Weight:		5,000 lbs. minimum, dry with cab

Comply Yes/No: _________________

Capacity:		Capable of sweeping a curb and gutter outside tires at a right or left sweeping angle

Comply Yes/No: _________________

Gradeability:		36%

Comply Yes/No: _________________

Engine:			Industrial type, 74 hp, water cooled diesel, 12 volt starter, heavy duty 12 volt battery, 50 amp alternator, variable speed governor, engine shall meet all current federal and EPA requirements.

Proposed Engine:	Make: __________________	Model: ___________	HP: _______

Comply Yes/No: _________________

Air Cleaner:		Dry type air cleaner, including a primary element, a safety element, an external-turbo pre-cleaner, evacuator valve secured with hose clamp, and a restriction (service) indicator.  The indicator is to be easily visible and mounted inside the operator’s compartment.  The pre-cleaner shall be mounted above the ROPS cab and substantially braced to with stand vibration.

Comply Yes/No: _________________

Transmission:		Complete hydrostatic drive with speed change made without mechanical gear movement.  It shall be a rear differential type drive axle with enclosed driveline.  The speed range shall be 0 - 20 mph.  Transmission designed to cushion shock of direction change speed. Gearbox not accepted.

Comply Yes/No: _________________

Frame:			All welded steel

Frame Type and Dimension: __________________________________________________

Comply Yes/No: _________________

Axles:			Front - heavy duty truck type - full oscillating

Rear - truck type - 1/2 ton capacity minimum

Comply Yes/No: _________________

Brakes:			Dry type, Four-wheel hydraulic with double master cylinder and mechanical parking, Wet type not accepted.

Comply Yes/No: _________________

Steering:		Hydraulic assist

Comply Yes/No: _________________

Tires:			Four (4) new 15" tires mounted on wheels of sufficient size to carry machine.

Size __________________

Comply Yes/No: _________________

Hydraulic

System:		spool control valves or electric over hydraulic controls for angling, lifting and lowering broom, and broom rotation.  Electric over hydraulic or spool controls to lock or float positions on machine.  Heavy duty oil cooler with a 10 micron filter having a replacement element, and having a 20 gal hydraulic oil capacity.

Comply Yes/No: _________________

Broom:			7’ 6” (minimum) wide with direct hydraulic drive encased in broom case and to operate independent of sweeper travel.  Rotation speeds up to 200 rpm.  Full cover over broom with end plates, core cover to be 140º - 16 gauge steel.  Broom to be capable of raising 2" above sweeping plane.  Filled with 32" diameter polypropylene wafer and steel wire brush in alternating section.

Comply Yes/No: _________________

ROPS Cab:		Fully enclosed, single sided entry cab (minimum), or, constructed of steel and tinted safety glass. Insulated cab floor with rubber grommets or boots around cab components that extend through the floor. Roll - over protective structure (ROPS) to meet the minimum requirements of SAE J1040C or latest revision

Comply Yes/No: _________________

Air Conditioner:		Minimum 13,500 btu/hr cooling with filtered cab pressurizer. Air flow, 250 cfm.

Comply Yes/No: _________________

Heater:			Minimum 12,500 btu/hr, and defroster fan.

Comply Yes/No: _________________

Wipers:			Powered windshield wipers, minimum one (1) front and one (1) rear with spray washers for both

Comply Yes/No: _________________

Instruments:		Tachometer, engine hour meter, fuel gauge, voltmeter or ammeter, temperature gauge, oil pressure gauge

Comply Yes/No: _________________

Lights:			Head and taillights, turn signals with 4-way flashers, brake lights.  Work lights for 360 degree visibility when working after dark or in low light/visibility settings. All other lamps and reflectors to meet federal and state regulations

Comply Yes/No: _________________

Warning Lights:		To be an amber LED strobe, 360 degree visibility, 12 volt, 2 amps, class 1, as listed in the MDOT vehicle safety lighting contract. The unit shall be mounted on top rear center of ROPS.

Comply Yes/No: _________________

Accessories:		Slow-moving vehicle emblems mounted, front and rear.  Adjustable suspension seat, mirrors - right and left, engine side shields, vandalism protection package, front bumper, back up alarm

Comply Yes/No: _________________

Paint:			Manufacturer's standard color

Comply Yes/No: _________________

ADDITIONAL REQUIREMENTS

Service:			Unit shall be delivered fully assembled ready to operate.  Factory-trained dealer representative is to inspect equipment on delivery and provide receiving MDOT equipment manager with information on operational, service, and maintenance requirements.

Acknowledge Yes/No: _______________

Warranty:		Clearly stated terms and conditions of all manufacturer warranties shall be included with the Statement of Qualifications (SOQ). Any and all materials, specialty equipment, or accessories that prove defective in normal operation within the warranty period shall be replaced or repaired by the manufacturer free of any and all cost to MDOT, including all material, labor, and transportation costs. Warranty replacement and/or repairs shall be furnished promptly by the successful bidder within a time period not to exceed thirty days. The bidder shall provide written assurance with the SOQ regarding warranty repairs.

The delivering dealer will have sole warranty responsibility (all components) for the first ninety days after acceptance of vehicle.

The manufacturer shall provide, with SOQ, a list of warranty service locations within the State of Mississippi for all components of the vehicle (A/C, body, chassis, electrical, etc.) which may need warranty repair beyond the first ninety days.

Acknowledge Yes/No: _______________

Workmanship:		Workmanship throughout the vehicle shall conform to the highest standard of commercially accepted practice for the class of work and shall result in a neat and finished appearance. The design of the body and equipment which the manufacturer proposes to furnish must provide a vehicle of substantial and durable construction in all respects.

All parts shall be new.  Used, reconditioned, or obsolete parts will not be accepted.

Acknowledge Yes/No: _______________

Parts Availability:	Dealer name and location within the State of Mississippi (if applicable):

Acknowledge Yes/No: _______________

Tests and Testing:	The complete vehicle and all working and moving parts and operating devices shall be thoroughly tested and put in operating condition by the manufacturer.

Prior to acceptance of vehicle by MDOT, the manufacturer shall service and adjust vehicle for operation.

Acknowledge Yes/No: _______________

Literature:		Technical manuals: Operator’s manual, service/maintenance manual, and parts book are to be made available in both hard copy and electronic (cd, flash drive, etc.) versions.  One set of technical manuals shall be provided with each unit upon delivery. Additional manuals may be ordered at a later date.

Technical service bulletins: Successful bidder shall provide TSBs (technical service bulletins) for all equipment delivered to MDOT as they are published, regardless of the date of delivery. TSBs may be furnished in paper or electronic format, and shall be updated regularly.

The following additional information shall be provided by the vendor at time of delivery (electronically if possible):

Manufacturer’s recommended service/preventive maintenance intervals

Recommended fluids, lubricants, and their SAE equivalents

Descriptive literature shall be furnished to substantiate the details specified in SOQ.

Acknowledge Yes/No: _______________

Certification:		The manufacturer(s) shall furnish certification that this machine meets or surpasses current U.S. Department of Labor Occupational Safety and Health Administration (OSHA) Regulations, U.S. Department of Transportation Federal Motor Vehicle Safety Standards (FMVSS), and any other applicable Federal regulations.

Acknowledge Yes/No: _______________

Vehicle Title or Certificate of Origin:

Assignment:	State of Mississippi/DFA – 941

Mailing address:	Mississippi Department of Transportation, 9301

P.O. Box 1850

Jackson, MS 39215

Acknowledge Yes/No: _______________

Lienholder:	Upon award, if MDOT issues a Notice to Proceed instead of a Purchase Order, the vehicle is being purchased through the State’s Master Lease Purchase Program, and the following shall be shown as the 1st Lienholder on the Title Application:

U.S. Bank National Association

Attention: Jacqueline McNeil

6810 Crumpler Blvd., Suite 200

Olive Branch, MS 38654

Lienholder Number: 90018867500

Acknowledge Yes/No: _______________