GREEN UNIKLEEN QX3

Introduction

GREEN UNIKLEEN QX3 is a highly effective variation of the basic environmentally friendly GREEN UNIKLEEN formula, with added ingredients to make it even more powerful.

Most detergents or cleaners used in industry today include ODS chemicals and the Freon haolhydrocarbon, which seriously destroys the earth’s ozone layer and does harm to ecological environment. The international agreement 《Montreal Protocol of Consuming Material about Ozone layer》has called on nations to stop producing and use this kind of matter by a set time。Therefore, developing and using environmental–friendly cleaner has become a priority.

Our product GREEN UNIKLEEN QX3 is a highly-effective, water-based degreaser, developed by American IPAX Corporation .It consists of non-toxic, environment-harmless penetrating grease dispersing agent and the emulsifier component .The key characteristic of this product is that it will not cause any damage to water, atmosphere, rivers and other water sources. Also, it has many unsurpassed characteristics, for example, versatility, environment friendly and highly-effect, neutrality. It can completely clean graphite, grease, dirt, stain, and tar.

Application scope:

GREEN UNIKLEEN QX3 is designed for the toughest parts washing and cleaning tasks.  It has been successfully used to remove hardened carbon from pistons and other parts.  QX3 works with all parts washer equipment, and works particularly well with ultrasonic units.

# Application Method

Application Dilution: The dilution ratio depends on cleaning job being done and the degree of the dirt .We suggests the ratio of 1Green Unkleen QX3 to 32 water. For heavy duty grease or for cleaning parts, a ratio of 1 part Green Unikleen to 8 parts water can be used.

Method: Can use the manual method to spray or to brush, but also can use the high-pressured machine to wash

Can be used in all kinds of cleaning machines, for example, heated dip tank, high pressured spraying machine, cold dip tank, steam sprayers, ultra sonic dip tanks, Vapor degreasing tanks, all parts equipment and etc. Better result appears when diluted with hot water

Notice:

Ingestion: Give copious quantities of fluids and seek medical attention

Keep closed when not in use.

Avoid: Storing Green Unikleen QX3 in extremely cold temperatures.

Keep away from children.