SAFETY DATA SHEET

LTDD

1.	CHEMICAL PRODUCT AND COMPANY IDENTIFICATION

Product Name:  LTDD

Product Description:  Low Temperature Dishwashing Detergent

MANUFACTURER:

Chemical Products & Systems

124 W. South St.

Jackson, Ms. 39201

601-354-1919

2.	HAZARDS IDENTIFICATION

GHS Classification:

Skin corrosion:			1A

Serious Eye Damage		1

GHS Label Element

Hazard Pictogram

Signal Word:			Danger

Hazard Statements:		Causes severe skin burns and eye damage.

Precautionary Statement:	Prevention:  Wash skin thoroughly after handling. Wear protective gloves/ protective clothing/ eye protection/ face protection.  Response:

IF SWALLOWED: Rinse mouth. Do NOT induce 							vomiting.

IF ON SKIN (or hair): Take off immediately all 							contaminated clothing. Rinse skin with water/shower. IF 						INHALED: Remove person to fresh air and keep 							comfortable for breathing. Immediately call a POISON 						CENTER or doctor/ physician. IF IN EYES: Rinse 							cautiously with water for several minutes. Remove contact 						lenses, if present and easy to do. Continue rinsing. 							Immediately call a POISON CENTER or doctor/ physician. 						Wash contaminated clothing before reuse.

Storage:			Store in a cool dry space away from heat and flames.  Keep 						out of reach of children.

Disposal:			Dispose of contents/container to an approved waste disposal plant.

.

3.	COMPOSITION/INFORMATION OF INGREDIENTS

Product as sold:			Mixture

Chemical Name				CAS Number   		Amount%

Sodium Hydroxide			1310-73-2	   	20-25

Amino tris (methylenephosphonic acid)	6419-19-8		1-5

Tetrasodium EDTA			64-02-8	    		1-5

Potassium Silicate			1312-76-1	    	1-5

4.	FIRST AID MEASURES

Eye Contact:	  		Flush eyes with plenty of water for 15 minutes.  Seek immediate 					medical attention.

Skin Contact:	  		Wash skin with plenty of water.  Remove contaminated clothing and 					shoes and wash before reuse.

Inhalation:	  		Although this product is not known to cause respiratory problems, if 					breathing is difficult, remove to fresh air and provide oxygen.

Ingestion:  			Rinse mouth with water.  Do not induce vomiting.  Never give anything 				by mouth to an unconscious person.    Get medical attention 						immediately.

Most important symptoms/effects, acute and delayed:  See section 11for detailed information.

Indication of immediate medical attention and special treatment needed, if necessary:

Notes to Physician:  		Treat symptomatically.

5.	FIRE FIGHTING MEASURES

Extinguishing media:		Use extinguishing measures that are appropriate to local circumstances 					and the surrounding environment.

Unsuitable extinguishing media:  	None

Specific hazards during firefighting:  Not flammable.

Protective Equipment and Precautions for Firefighters

As in any fire, wear self-contained breathing apparatus pressure-					demand, MSHA/NIOSH (approved or equivalent) and full protective 					gear.

6.	ACCIDENTAL RELEASE MEASURES

PERSONAL PRECAUTIONS:  	Ensure adequate ventilation.  Use personal protective equipment.  					Avoid contact with clothing, skin and eyes. Stop leak if safe to do so.

Environment Precautions:	  Do not allow contact with soil, surface or ground water.

Protective Equipment:		 Use personal protective equipment.  See section 8.

Methods and materials for cleanup:  Stop leak if safe to do so.  Contain spill and absorb 						material with earth, sand or other non-combustible material and transfer 				to containers for disposal.  Rinse area with water.

7.	HANDLING AND STORAGE

Handling:  			Avoid contact with clothing, skin and eyes.  Where contact is likely, 					wear chemical resistant gloves, rubber boots, and chemical goggles 					plus a face shield. Do not eat, drink or smoke when using this product. 					Do not take internally. Wash thoroughly after handling.

Storage Precautions: 		Keep tightly closed and store in a cool dry place.  Keep away from heat 				and flame.  Keep from freezing.

8.	EXPOSURE CONTROLS/ PERSONAL PROTECTION

Occupational Exposure Limits:  	No occupational exposure limits have been established for this product

Engineering Controls:  		Effective exhaust ventilation system.

Personal Protective Equipment:

Eye Protection:			Wear safety glasses, goggles or eye shield

Skin Protection:  		Wear protective gloves to minimize skin contamination.  						Wear appropriate personal protective equipment.

Respiratory Protection:  		In case of inadequate ventilation, wear suitable respiratory equipment.

9.	PHYSICAL AND CHEMICAL PROPERTIES

Appearance:				Liquid

Color					Red

Odor:					Slight ammonia-like odor

Odor Threshold				No data available

pH					>14

Viscosity				No data available

Vapor density:				No data available

Specific Gravity:				1.3

Flash Point				Not applicable

Boiling Point:				No data available

Vapor pressure:				No data available

Partition coefficient			No data available

Autoignition temperature			No data available

Decomposition temperature		No data available

VOC					No data available

Flammability				No data available

Solubility in water:			Soluble

Melting/freezing point:			No data available

10.	STABILITY AND REACTIVITY

Stability:  				Stable under normal conditions.

Polymerization:  			Will not occur.

Incompatibility: 				Not compatible with acids and oxidizers.

Hazardous decomposition products:	Oxides of Carbon, Nitrogen and Phosphorous.

11.	TOXOLOGICAL INFORMATION

Likely Routes of Exposure:		Inhalation, Eyes and Skin contact

Potential Health Effects:

Eyes:					Causes severe eye damage

Skin:					Can cause severe burns

Ingestion:				Causes digestive tract damage

Inhalation:				May cause irritation to nose, throat and respiratory tract.

Chronic Exposure:			None known

12.	ECOLOGICAL INFORMATION

When used for its intended purpose this product has no known Environmental effects.

13.	DISPOSAL CONSIDERATIONS

Disposal Methods:			Dispose of waste material in accordance with all Federal, State 					and local regulations.

14.	TRANSPORTATION INFORMATION

UN Number:				UN1824

Proper Shipping Name:                               Corrosive Liquid, Basic, Inorganic, n.o.s. (Sodium

Hydroxide solution)

Hazard Class:				8

Packing Group:				II

15.	REGULATORY INFORMATION

This product contains the following component(s) which is subject to the reporting requirements of SARA Section 302, SARA Section 313 and /or CERCLA

Sodium Hydroxide			CAS No. 1310-73-2

CERCLA Final RQ:			1,000 lbs.

16.	OTHER INFORMATION

This information is furnished without warranty, expressed or implied, except that it is accurate to the best knowledge of Chemical Products & Systems.

Reason for revision:  GHS format