INSTRUCTIONS TO BIDDERS AND SPECIFICATIONS

LEAKE COUNTY BOARD OF SUPERVISORS

Leake County Courthouse

Court Square

P. O. Drawer 72

Carthage, MS  39051

RE:	Track Hoe

BID DUE DATE:	9:00 O'CLOCK A.M., MAY 15, 2017.

WRITTEN SEALED BIDS TO BE FILED BEFORE ABOVE TIME AT THE OFFICE OF THE CHANCERY CLERK OF LEAKE COUNTY, LEAKE COUNTY COURTHOUSE, CARTHAGE, MISSISSIPPI, OR MAY BE MAILED TO THE ABOVE ADDRESS.

INSTRUCTIONS TO BIDDERS

1.	The Board of Supervisors is acting under the authority of Section 31-7-13, Mississippi Code of 1972, as amended, and reserves the right to reject any and all bids.

2.	All bids must be sealed and the outside envelope clearly marked in the following manner:

Bid: Track hoe

May 15, 2017, 9:00 A.M."

Otherwise the bid will not be considered.

3.	The above-described machinery must be in new and unused condition, and such new and unused condition must be represented in the bid.

4.	Any exceptions to the above specifications must be listed in the bidders bid.  Failure to do so will disqualify the bid.

5.	All bids must state delivery time (which will be a factor used in determining the lowest and best bid), and bid price must include delivery to the Leake County Maintenance Facility at 312 C.O. Brooks St., Carthage, Leake County, Mississippi.

6.	All bids must state warranty, if any, which will be a factor used in determining the lowest and best bid.

7.	Expenses for the development and delivery of proposals are entirely the responsibility of the vendor and shall not be chargeable to the county.

8.	Any bid not received in writing at this office by the date and time specified will be declared a late bid.  The Board will not be responsible for any delays in delivery.  It is solely the responsibility of the vendor that proposals reach the bid opening on time.  Any bid received after bid-closing time will be returned unopened.

9.	Bids or alterations by wire or phone will not be accepted.

10.	All bid openings are open to the public.  The Board will read a summary of each vendor's bid and answer all questions to the extent possible at the time.  Any information provided in the bid which contains trade secrets or confidential commercial or financial information and which bidder does not wish to be disclosed other than for purposes of evaluation, must be clearly labeled on each as confidential.  All confidential information must be bound separately from other bid documents.

11.	No negotiations, decisions or actions shall be executed by any bidder as a result of any discussions with any county employee or board member.  Only transactions, which are in writing from the Board, may be considered official.

12.	The Board reserves the right to reject any and all bids and to waive any defect or informality in any bid or bidding process.

13.	If the Board accepts a bid in response to this Request for Proposal, it will accept the bid and award the contract to the lowest and best responsive bidder meeting specifications, price and other factors considered.  Other factors to be considered include, but are not limited to, conformity to the specifications; quality; bidder's performance on contracts with other political subdivisions; and consideration will be given to the proximity of support offices.

14.	All proposal material submitted in writing shall become the property of the county.

SPECIFICATIONS FOR TRACK HOE

The following are the minimum specifications for a Track Hoe.  All bids must be equal in performance and quality to the following specifications, which are not intended to exclude any manufacturer.  Any reference to manufacturer's make or series of equipment stated in the following specifications are intended only to establish an acceptable standard and are not intended to limit the bidding.

1. 	Engine gross power shall be no less than 120 hp (90 kW)

2. 	Operating weight for a long undercarriage, 10’ 2” (3100 mm) stick and 28" shoes shall be no less than 38,800 lbs. with a 48" bucket.

3. 	Lift capacity at 20’ (6 m) over the front at ground level shall be not less than 10,000 lbs. with 28" (600 mm) shoes, long undercarriage, and 10’ 2” (3100 mm) stick.

4. 	Lift capacity at 20’ (6 m) over the side at ground level shall be not less than 5800 lbs. with 28" (600 mm) shoes, long undercarriage, and 10’ 2” (3100 mm) stick.

5.	Ground clearance shall be not less than 18” (440 mm).

6. 	Maximum digging depth shall be 21’ with a 10’ 2” (3100 mm) stick.

ENGINE

7. 	Engine shall meet US EPA Tier 4 Interim and EU Stage IIIB emission requirements requiring no DEF Fluid.

8. 	Four-cylinder diesel engine shall be provided and made by the Machine Manufacturer.

9. 	Machine shall have a one touch low idle system.

10. 	Engine shall have a standard electric fuel priming pump.

POWERTRAIN/TRANSMISSION

11. 	Travel speed shall be at least 3.0 mph

12. 	Maximum drawbar pull shall be 156.2kN (35,115 lbs. ft.)

13.	 A49Draw bar pull shall be at least 34,000lbs

UNDERCARRIAGE

14. 	Machine shall have as an option 700 mm (28 inch) triple grouser shoes

OPERATORS STATION

15. 	Machine shall have a Certified ROPS Cab with Air conditioning and Heating.

16. 	A rotary dial shall be provided to control engine speed.

17. 	Machine shall have a system that checks the following fluid levels upon machine start-up and warns the operator if the levels are not within acceptable ranges: Engine oil level, engine coolant level and hydraulic oil level.

18. 	A pattern control changer shall be available.

STICK AND BOOM

19. 	SAE Stick digging force shall not be less than 16,000 lbs. with a 10’ 2” (3100 mm) stick.

20. 	Maximum reach at ground level shall be at least 30’ 5” (9260 mm) with at 10’ 2” stick.

21. 	Maximum loading height shall be at least 20' with a 10’ 2” (3100 mm) stick.

SWING SYSTEM

22. 	Swing torque shall be at least 32,000 lbs - ft

23. 	Swing speed shall be at least 9.2 rpm.