FOR PUBLICATION IN ISSUES OF: Monday, November 10, 2014, and Monday, November 17, 2014

# NOTICE TO BIDDERS

Notice is hereby given that bids will be received by the City Clerk of the City of Pascagoula, Mississippi, at City Hall during legal office hours until 2:00 P.M., Thursday, December 4, 2014, at which time all bids will be publicly opened in the Council Chambers of the City Hall and read aloud for the following:

Asphalt          Annual Bid #349A for Type BB-1 (Application on prepared sub base)

Asphalt          Annual Bid #349B for Type SC-1  (Overlaying existing pavement)

All bids shall be submitted in a sealed envelope addressed to the City Clerk of the City of Pascagoula, Mississippi. If a bid is submitted by mail, the post office address of the City Clerk is 
P. 0. Drawer 908, Pascagoula, Mississippi 39568-0908. If a bid is hand-delivered, the street address of the City Clerk is 603 Watts Avenue, Pascagoula, Mississippi 39567-4220.

All bid envelopes shall be marked "SEALED BID TO BE OPENED AT 2:00 P.M., Thursday, December 4, 2014", and if any envelope is not so marked, any bid contained therein will not be considered.

All bid envelopes must contain the bidder's name and mailing address on the face of the envelope and also specify the name of the bid item.

Specifications and bid information may be obtained at the office of the Purchasing Agent at 
630 Delmas Avenue, Utilities Accounting Building, during legal office hours. The phone number is 
(228) 762-1020 or (228) 938-6722. Email is rwood@cityofpascagoula.com. This information is also available online at http://cityofpascagoula.com/purchasing.

The City reserves the right to reject any or all bids, to waive informalities and, when multiple items or supplies for a period of time are involved, to award bids on an item by item basis to separate bidders.

No bid may be withdrawn for a period of thirty (30) days after the above bid opening date.

BID FOR FURNISHING PLANT MIX BITUMINOUS BASE COURSE,

TYPE BB-1 (FOR APPLICATION ON PREPARED SUBBASE)

BID #349A

This bid is for a period of twelve months with a twelve-month renewal option by the City of Pascagoula, or shall remain in force until a new contract has been awarded.

Plant mix bituminous base course, Type BB-1, in place on prepared subbase roads complete, including furnishing and placing required tack coats and plant mix bituminous base course, together will all necessary tools, equipment and labor.

Specifications

- Plant mix bituminous base course, type BB-1 shall conform to Section 301, MSHD Specifications for State Aid Road and Bridge Construction, 1989 Edition.

- Weight tickets from certified scales shall be issued for each load from bidder’s plant.  Scale tickets shall be signed by a representative of the City of Pascagoula.

- The contractor installing the asphalt is responsible for providing traffic control in accordance with the latest edition of the Manual of Uniform Traffic Control Devices.

- The successful bidder shall fill orders within 24 hours of placement thereof by the City.  Should the successful bidder fail to do so within the 24 hour period, the City shall be at liberty to purchase the ordered material from others and the successful bidder shall be liable to the City for any additional cost incurred by reason of the bidder’s failure to supply within the time specified.

- The plant shall meet the requirement of Section 401.10 of the Mississippi Standard Specifications for State Aid Road and Bridge Construction.

BB-1 price per ton $____________ laid in place

I do hereby certify by my signature that our products bid meet or exceed your specifications.  I agree that failure to meet the specifications shall be just cause for the City of Pascagoula to remove our company from the bid list.

__________________________________		______________________________

Company Name 					City Privilege Tax License Number

__________________________________		______________________________

Street or Mailing Address				Phone Number            Fax Number

__________________________________		______________________________

City, State and Zip Code				Email Address

__________________________________		______________________________

Signature of Authorized Representative		Date

BID FOR FURNISHING HOT BITUMINOUS PAVEMENT,

TYPE SC-1 (FOR OVERLAYING EXISTING PAVEMENT)

BID #349B

This bid is for a period of twelve months with a twelve-month renewal option by the City of Pascagoula, or shall remain in force until a new contract has been awarded.

Hot bituminous pavement, type SC-1, in place for overlaying existing pavement or application on previously prepared base course, including furnishing and placing required tack coats and hot bituminous pavement together with all necessary tools, equipment and labor.

Specifications

- Plant mix bituminous base course, type SC-1 shall conform to Section 403, MSHD Specifications for State Aid Road and Bridge Construction, 1989 Edition.

- Tack coat shall be emulsified asphalt grade EA-4 or cutback asphalt grade RD-30, meeting requirement of Section 702, MSHD Standard Specifications for State Aid Road and Bridge Construction, 1989 edition.  No measurement or payment will be made for materials used for tack coats.

- Weight tickets from certified scales shall be issued for each load from bidder’s plant.  Scale tickets shall be signed by a representative of the City of Pascagoula.

- The contractor installing the asphalt is responsible for providing traffic control in accordance with the latest edition of the Manual of Uniform Traffic Control Devices.

- The successful bidder shall fill orders within 24 hours of placement thereof by the city.  Should the successful bidder fail to do so within the 24 hour period, the City shall be at liberty to purchase the ordered material from others and the successful bidder shall be liable to the City for any additional cost incurred by reason of the bidder’s failure to supply within the time specified.

- The plant shall meet the requirement of Section 401.10 of the Mississippi Standard Specifications for State Aid Road and Bridge Construction.

SC-1 price per ton $____________ laid in place

SC-1 price per ton $____________ picked up at plant

I do hereby certify by my signature that our products bid meet or exceed your specifications.  I agree that failure to meet the specifications shall be just cause for the City of Pascagoula to remove our company from the bid list.

__________________________________		______________________________

Company Name 					City Privilege Tax License Number

__________________________________		______________________________

Street or Mailing Address				Phone Number            Fax Number

__________________________________		______________________________

City, State and Zip Code				Email Address

__________________________________		______________________________

Signature of Authorized Representative			Date