Decatur Special Infrastructure Project Scope of Work:  Drainage, Curbing and Guttering

Base Quote:

- N 8th Ave Drainage Improvement: Install 2 each  storm water collection boxes near 245 and 255 N 8th Ave. The actual location will be marked with flags.  The southernmost storm water box will tie into an existing 14 inch id concrete culvert that runs across street. The northernmost storm water collection box will be set approximately 120 ft north and the two storm water boxes will be connected with 12 inch plastic culvert. The storm water drains will be fitted with road worthy steel grates.

- N 8th Ave Curb and Gutter Installation:  Install approximately 1300 lf of 18-inch wide curbing and gutter on the west side of the street from West Broad St to 10th Street

Grade, excavate and fill-in as appropriate, compact soil and/or gravel to provide good curb & 	gutter foundation

-Curb and gutter to be rolled downward—the gutter needs to be lower than the 				road.

-Curb and gutter to be installed to provide sufficient drainage & fall

-The gutter should extend up 1 ½ inch over existing average road level at gutter to 			accommodate 1 ½ inches of asphalt that will be laid.

-Back-fill and level dirt on the backside of the curbing for sufficient water drainage.

-Adjust driveways (9 in total) as appropriate to ensure sufficient water flow.

-any driveway modifications need to be at a an adequate slope to prevent car 				bumpers from dragging.

-re-pour any driveways that require modifications

Alt A Quote: Install 600 lf of 18 inch wide Curb and Gutter on the  north side of N 5th Ave from the 			Hwy 15 ROW marker to the turn in the N 5th Ave road

Curbing and guttering specs as above. There are no driveways.

The contractor will provide a written fixed fee quote for all labor and equipment to perform the scope of work for both the Base Quote and for the Alt A case.  The town will provide materials (culverts, concrete, forming materials, etc.) for the job.

Contractor written quote is to be valid for 30 days and the work must be commence within 30 days of contract award and all work to be completed within 45 days.

The successful contractor needs to comply with the Mississippi Employment Protection Act of 2008.

There are only sketches of the work to be completed. Interested parties should base their bids on a visual inspection of the area. Work will be completed to the satisfaction of the Public Works Director-David Anderson.

Summit written quotes to:

Town of Decatur

Attn: Pat ONeill—Special Infrastructure Quote

PO Box 307

Decatur, MS 39327

by April 24, 2017 at 10 am CDT at the latest