INVITATION TO SUBMIT SEALED BIDS

Buyer - Simpson County Board of Supervisors

Date of Bid:	Tuesday, July 18, 2017

Time of Bid: 	10:00 a.m.

Location:	Meeting room of the Simpson County Board of Supervisors, Simpson County Chancery Building, 111 West Pine Ave., Mendenhall, Mississippi  39114

AT THE ABOVE DATE AND TIME, SEALED BIDS WILL BE ACCEPTED FOR:

One Used hydraulic excavator.  Equipment shall be 2014 year model or newer, in good working condition, with the following minimum specifications:

No more than 425 hours.

No less than 91 net horsepower water cooled 260 cubic inch diesel engine meeting tier IV standards – Non DEF Unit.

Enclosed Cab with Heat and Air Conditioning.

Hydraulics (minimum) 467 total gallons per minute,

34 Swing system gallons per minute,

Electric boom regeneration system,

Auxiliary Hydraulics stubbed off at the cab,

Fine swing control.

Minimum weight 30,000 lbs.

Equipped with all standard equipment, a manual thumb, jump start receptacle, AM/FM Radio, two power outlets, sunscreen, two speed travel, economy & high-power mode, grease lubricated track, towing eye on base frame, 28” Grouser track shoes.

Warranty for minimum through March 28, 2019 or 5,000 hours (whichever comes first) for powertrain and hydraulics.

Lease purchase option with 3, 4 and 5 year lease terms and monthly payments.

Delivery time may be a factor in determining the lowest and best bid.

Bids shall be sealed and the outside envelope shall be clearly marked “Used Excavator and/or Lease Purchase Financing”, as appropriate, along with the date and time of the bid opening.  The award will be made to the lowest and best responsible bidder meeting the requirements of the specifications in accordance with Section 31-7-13, Miss. Code of 1972, Ann.  The buyer will not be responsible for bids opened in error, which are incorrectly or inadequately marked.

The buyer reserves the right to reject any and all bids with or without cause.

No bid may be withdrawn for a period of thirty (30) days.  Bid price shall be valid for 2 months after bid acceptance.  No additions or modifications will be allowed after the bids are opened.

Return Bids to:

Simpson County Board of Supervisors

Mail:	P.O. Box 308			Physical:	Simpson County Chancery Bldg.

Mendenhall, MS  39114			111 West Pine Ave.

Mendenhall, MS 39114

(Publish 2 times:  June 29, 2017 and July 6, 2017)