ANNUAL BID #343

COVERS, FRAMES AND GRATES SPECIFICATION

The City of Pascagoula is seeking an annual bid on the following Covers, Frames and Grates.  The contract shall be for a one-year period of time from the date of Council approval and contains an automatic one-year renewal option at the same price or current contract shall remain in force until a new contract has been awarded.

- Materials

  - Ferrous castings shall be of uniform quality. Free from blowholes, shrinkage, distortion or other defects.  They shall be smooth and well cleaned by shot blasting.

  - Quality:  Metal used in the manufacture of castings shall conform to ASTM A48-76 Class 35 for gray iron or ASTM A536-80 Grade 65-45-12 for ductile iron.

  - Finish:  All castings shall be manufactured true to pattern; component parts shall fit together in a satisfactory manner.

  - Tolerances:  As cast dimensions may vary one-half the maximum shrinkage possessed by the metal or +/- 1/16 inch per foot.

  - Weight:  All published weights are average (and approximate) values.  Deviation shall not exceed published weights by +/- 5 percent.

  - Covers:  Shall have continuously machined bearing surfaces to prevent rocking and rattling.

  - Equals:  Manufacturer names, catalog numbers or specifications are used for the purpose of establishing a standard of quality and the facilitating of the descriptions of the material or process desired.  This procedure is not to be construed as eliminating from competition other products of equal or better quality by other manufacturers where fully suitable in design.  The bidder may submit complete data (i.e. catalog numbers and drawings) for consideration.

- Miscellaneous

The City reserves the right to reject any or all bids, to waive informalities and when multiple items or supplies for  a period of time are involved, to award bids on an individual basis or an all or none basis, whichever is in the best interest of the City of Pascagoula.

ANNUAL BID #343

COVERS, FRAMES AND GRATES,

CITY OF PASCAGOULA BID SHEET

ONE COMPLETE UNIT:  COVERS, FRAME, AND GRATE

Light Duty Manhole Ring and Cover				$_____________Unit Price

Highway Standard Manhole Ring & Cover			$_____________Unit Price

Grated Ring and Cover for Manhole				$_____________Unit Price

GRATE:

Stool Type Grate Equal to Vulcan V-6489			$_____________Unit Price

FRAME AND GRATES TO FIT INSIDE PIPE:

12”			$_________________Unit Price

15”			$_________________Unit Price

18”			$_________________Unit Price

24”			$_________________Unit Price

30”			$_________________Unit Price

12” x 12”		$_________________Unit Price

18” x 18”		$_________________Unit Price

24” x 24”		$_________________Unit Price

26” x 26”		$_________________Unit Price

30” x 30”		$_________________Unit Price

F.O.B. 4011 14th Street, Pascagoula, MS  39567

This contract contains an automatic one-year renewal option, or shall remain in force until a new contract has been awarded.

________________________________    		________________________________

Company						Address

________________________________ 		________________________________

Authorized Signature				  Phone & Fax Number