SPECIFICATION FOR BUCKET TRUCK

BID # 352

The City of Pascagoula (City) is requesting bids for a bucket truck. The use of brand name specifications and drawings is to provide prospective vendors with a product standard and/or guidelines for equipment needed; all equipment meeting or exceeding the brand name specifications used will be given equal consideration. The City of Pascagoula will be the sole judge of equipment that is submitted as equal and the decision of the City of Pascagoula shall be final.

GENERAL:	The City of Pascagoula reserves the right to reject any or all bids, to waive informalities and when multiple items or supplies or a period of time are involved, to award bids on an individual basis or on all or none bases, whichever is in the best interest of the City of Pascagoula.

RESPONSIBILITY OF BIDDERS:  All bids submitted shall have included in price the cost of any business and professional licenses, permits, and fees required by the City of Pascagoula. All bidders shall include with their bids a Mississippi State License number.  All bidders shall include with their bids their Federal Identification number.  All equipment shall meet local, state, and federal codes and standards.

INSURANCE:  The contractor shall purchase and maintain in force, at his own expense, such insurance as will protect him and the City from claims which may arise out of or result from the Contractor’s execution of the work, whether execution be by himself, his employees, agents, subcontractors, or by anyone for whose acts any of them may be liable.

EQUIPMENT REQUIREMENTS

It is the intent of these specifications to describe the minimum specifications for the bucket truck.  Standard equipment and accessories will be those stated in the manufacturer’s published literature, except when modified to meet these specifications.  Standard product items shall be removed only when necessary to install other items in lieu thereof to comply with these specifications.

Standard Features:

1. Platform capacity of 400 lbs. (180 kg) with jib installed, 500 lbs. (225 kg) with jib removed (available on chassis with 19,000 GVWR or higher only)

2.  UNITROL single stick upper control with emergency stop/dump valve and tool selector

3.  Individual full-pressure lower controls at the turret actuate all boom functions

4.  180 degree hydraulic platform rotator

5.  Engine start/stop form platform

6.  Continuous rotation including slip rings

7.  Six gpm (22.7 lpm) open center hydraulic system; operating pressure is 2500 psi (175 kg)

8.  Side mounted telescopic upper boom allows low stowing of platform; fiberglass inner boom and patented ELECTROGARD provide insulation gap fully retracted meeting ANSI A92.2-2001 for Category C, 46 kV and below

9.  Self-locking worm gear rotation drive with shear ball bearing

10.  Chassis insulating system (fiberglass lower boom insert) providing 12 in. (0.30m) insulation gap and including accommodations to bridge insulation gap for testing per ANSI A92.2-2001

11.  Material handling jib and winch with 800lbs. material handling capacity and automatically levels with platform; hydraulic extension/retraction and hydraulic articulation are included

12.  ELECTROGARD and inner boom finished with white urethane paint over a white gel coat

13. Non-lube bearings used throughout

14.  One set hydraulic tool outlets at platform; quick disconnect fittings are not included

15.  Integral hydraulic oil reservoir with dual sight gauges and 17-gallon (64.41) capacity;  bottom suction with a gate valve is provided

16.  Closed heavy-duty one step 24 in. x 30in x 42 in. (.61m x .76 x 1.07m) fiberglass platform with liner and vinyl cover

17.  Master/slave hydraulic leveling with upper control to tilt for cleanout or rescue

18.  Upper boom storage cradle with ratchet type tie down strap and tubular rubber platform support

19.  Main hydraulic A-frame outriggers and hydraulic Rear outriggers

20.  Emergency power

21.  Mounting hardware

22.  Unit painted standard white

23.  Safety harness and lanyard

24.  Two operator’s and two service manuals

25.  ANSI A92.2-2001 data plate

Body

Brand FX 132” x 40” high fiberglass service body

Street-side Compartments:

1st Vertical:  Two adjustable shelves /dividers

2nd Vertical:  Two adjustable shelves w/dividers

Horizontal:  Divider Tray (Bottom)

Rear Vertical:  Open      Rear Vertical:  Locking swivel Hook 1-3-1

Lighted tool compartments

Curbside Compartments:

1st Vertical:  Two adjustable shelves w/dividers

2nd Vertical:  Two access steps

Horizontal:  Divider Tray (Bottom)

Lighted tool compartments

Hot stick shelf street-side with door

Aluminum tread-plate floor and 24 inch tail-shelf with cable type stirrup step

LED light kit with standard back-up lights

Wheel Chock Holder (Fenders)

Cab/Chassis

2015 Dodge 5500 SLT 4x2 cab and chassis

19,000 lb. GVWR

PTO Provision

I-6 6.7 Cumming Diesel

Heavy duty AISN 6-speed transmission

84 inch CA

4.44 axle ratio w/ Limited Slip

AM/FM radio; A/C

220 AMP Alternator

Daytime running lights

4 Upfitter electronic accessory switches

4 Rear traction tires

Installation

Install mounting hardware, PTO, and pump

Install VERSALIFT VST-240-MHI

Install hydraulic A-frame outriggers

Install hydraulic Rear outriggers

Install 2” receiver hitch

Install 6 prong trailer plug and electric brake controller

Install two (2) LED amber rotating strobe beacon and post mount

Install 4 corner LED strobe light system

Install 2 low profile LED strobe lights on top of service body left and right side

Install 2-6 inch Unity deck mounted work lights mounted at front corners of body

Install 1-poly tool tray 8” x 19” x 8”

Install back up alarm

Install parking brake interlock

Install two (2) cable steps

Install mud flaps

Furnish 18” x 18” outrigger pads and rubber wheel chocks

Paint tread plate floor with black no-skid

Furnish 3 piece triangle reflector kit

Test ride completed unit for one hour

Test and Certify per ANSI A92.2-2001

WARRANTY:  To obtain warranty service, the purchaser shall notify the manufacturer, in writing, at the address provided, within the warranty period, and the manufacturer will direct where to take or send the equipment for service.  If the defect is covered by the warranty, the manufacturer will repair or replace, at its option, the defective equipment, without charge for labor or materials (freight and insurance are the purchaser’s responsibility).  This warranty is limited to the original retail purchaser.  The manufacturer assumes no responsibility for damage due to accident, neglect, abuse, tampering, misuse, or damage from repairs or alterations by others.  The manufacturer’s sole obligation and the original retail purchaser’s exclusive remedy under this warranty shall be for repair or replacement as described above.  All other warranties, whether expressed or implied, including but not limited to implied warranties of merchantability and fitness for a particular purpose, are disclaimed.  In no event shall the manufacturer be liable for any incidental or consequential damages.  Under no circumstances is loss of time, revenue, or consequential damages covered under this warranty.

REFERENCE:  Current Owner – A list of at least five (5) current owners, including their address and telephone number, who currently own a bucket truck similar in nature to the unit proposed by the contractor shall be submitted with the bid package.  This will allow the City of Pascagoula to obtain first-hand information as to the quality and reliability of the proposed equipment.  Owners submitted shall be as geographically near to the City of Pascagoula as possible.

Contractor History and Information – The Contractor shall submit evidence that the manufacturer has been continuously in the business of producing equipment similar to that specified herein for the last fifteen (15) years.

SERVICE CENTER:  Certified Service Center – The Contractor shall provide as an attachment or part of the warranty information the manufacturer’s certified service center best suited logistically to repair/service the equipment as needed.  This information shall only include the name, address and the telephone number of this service center.

EQUIPMENT RECORDS: Successful bidder shall be responsible for preparing and maintaining a record file of all parts and assemblies used to manufacture the equipment and furnish the City of Pascagoula with copies of all updates.  Additionally, these records shall be maintained in the factory/office of the bidder for the life of the equipment.  File shall contain copies of any and all reported deficiencies, all replacement parts required to maintain the equipment, and original purchase document, including specifications, contract, invoices, complete chassis certificate, quality control reports and final delivery acceptance documents.  The City of Pascagoula shall have access to any and all documents contained in this file upon request.

FIXED BID AMOUNTS:   Bid shall remain firm for sixty (60) days.  The bid amount accepted through this bid shall remain for sixty (60) days from the bid opening date.  This will allow careful examination of the bid package and submitted documents in order to determine compliance with the stated requirements and specifications.

Total Bid:  $______________________

All bid prices shall be F.O.B. destination: 4011 14th Street, Pascagoula, MS 39567.

Questions regarding this bid shall be directed to Jeff Hutchison, City of Pascagoula Public Works-Water Department, at (228) 217-2699 during normal business hours, Monday – Friday.

_______________________________	______________________________

Company Name				Authorized Signature

_______________________________	______________________________

Address					City/State/Zip

_______________________________	______________________________

Phone		Fax