# NOTICE TO BIDDERS

Notice is hereby given that Lafayette County, Mississippi will receive written sealed bids until 10:00 A.M. on Wednesday, December 10, 2014, for the purchase and/or lease purchase of One (1) or more new 2015 Model Year Tandem Axle Day-Cab Tractor.

Instructions to Bidders:

- No responsibility will be attached to any person employed by Lafayette County, Mississippi, for the premature opening of any bid not properly addressed and identified as stipulated below:

BID 305 – 2015 Tandem Axle Day-Cab Tractor

OPENING TIME/DATE 10:00 A.M., December 10, 2014

- All equipment / trucks offered in the bid must be new and in unused condition.  Only 2015 year models will be considered

- Any exceptions to the specifications must be listed in the Bidders bid with justification.  Failure to do so will disqualify the bid.

- Price bid shall be for F.O.B. 142 Highway 7 South, Oxford, MS , and must include any pre-delivery and/or setup charges, title fees and inspection fees.

- The Bidder shall complete the unit price bid with no further calculations required in order to determine the firm unit price.

- Bid must be signed and dated by the Bidders Authorized Agent.

- All bids must state Manufacturer Warranty.

- All bids must state approximate delivery time.

- Locations for parts and service must be included in the bid and will be a factor in determining the best bid.

- All Bidders must secure a bid sheet along with specifications.  Bid sheet must be completed in entirety before submission as a formal bid.

- All Bidders must offer a guaranteed residual at the end of the term specified on “Bidders Sheet”.  All terms, conditions, and/or limitations specific to the equipment at time of turn in must be clearly stated.

- It shall be incumbent upon each Bidder to understand the specifications on the bid form and to obtain clarification when necessary.  It is not the intent of the specifications to limit the bidding process to any make or manufacturer, but to fill a specific need and to perform a specific task.

- All bids must include a trade value per unit on the listed equipment included in the bid package. No bids shall be considered without the trade values included.

- The Lafayette County Board of Supervisors reserves the right to determine which is the lowest and best bid and to accept or reject any or all bids based on that determination.

- Questions per the above should be directed to:

Joseph Johnson,

County Administrator

300 North Lamar Boulevard

Oxford, MS 38655

(662)236-2717

jjohnson@lafayettecoms.com

Bid Sheet

Sales Price: _______________________________

Trade Value_______________________________

Payment Amount: __________________________

Guaranteed Residual: _______________________

Term: ____________________________________

Interest Rate: ______________________________

Lessor Name: ______________________________

Lessor Address: ____________________________

Lessor City/State/Zip: _______________________

Contact: __________________________________

Contact Phone Number: ______________________

Primary Email Address: ______________________

# Lease Expenses:

Please Provide the Following Information:

Indicative Interest Rate: ______________________

Please state ALL Terms & Conditions applicable to the financial package proposed.

NOTE:  Bidder must quote simple interest only with no pre-payment penalty for

Early Payoff.

____________________________

Authorized Signature

____________________________

Date

Bid Specifications

Tractor to Pull Dump Trailer

Complete by Checking the Following

IF NOT COMPLIANT, state Specifically the item being offered

YES    NO	 OFFERED

# Wheelbase/Frame

Wheelbase  213”						(	(	___________

CA 120”							(	(	___________

Platform 182”							(	(	___________

AF 56”								(	(	___________

Frame Rails – 10.47” X 3.54” X .275”			(	(	_______

with 1,600,000 in lbs. per rail

Bright Finish Bumper						(	(	___________

HD Crossmembers						(	(	___________

## Air Slide Fifth Wheel, 7.75” Legs, Factory No Tilt		 (	(	___________

## Rear Mud Flaps						(	(	___________

Chrome Quarter Fenders					(	(	___________

## Wet Kit – Hydraulic Kit to pull Dump Trailer		(	(	___________

## Engine

- Electronic 4-cycle diesel, in line 6 cyl., Turbocharged with air-to-air inter-cooler, minimum 700 cubic inch sleeved engine, 13 Liter minimum of 445 HP with 1735 ft/lbs. torque, all spin-on filters (fuel, oil, water).  NOTE: Bids will be accepted only with engines certified by the EPA to meet 2010 EPA regulations

(0.2 Nox and 0.01 Particulate Matter – both measured using the EPAs 0.02 formula of [g/bhp – hr]) at the tailpipe.																(	(	__________

YES    NO        OFFERED

## Air Compressor – 18.7 CFM					(	(	___________

Alternator – 12V 135A 35 SI					(	(	___________

Batteries – Group 31 650/1950 Threaded Stud Type		(	(	___________

Bug Screen							(	(	___________

Coolant Protection Extended Life to –34 Degrees F(		(	(	___________

Engine Block Heater 						(	(	___________

Fan Drive – Borg Warner Cool Logic			(	(	___________

Fuel-Water Separator						(	(	___________

Engine Brake							(	(	___________

Starter – 12-Volt						(	(	___________

Exhaust – Dual Vertical Straight Exhaust			(	(	___________

With Bright Finish Heat Shields and Stacks

## Diesel Particulate Filter Frame Mounted RH side		(	(	___________

## Under Cab

## Transmission/Clutch/Drive Lines

Clutch: Eaton Advantage solo 9 spring			(	(	___________

Transmission – 10 spd.					(	(	___________

Flywheel Housing – Aluminum				(	(	___________

Transmission Oil Cooler					(	(	___________

YES    NO        OFFERED

Synthetic Fluid 						(	(	___________

Driveline Main Spicer 1810 HD				(	(	___________

Driveline – Interaxle Spicer 1710 HD			(	(	___________

# Front Axle

Front Axle – 12,000 lb/ Axle Forward			(	(	___________

Springs – Taper-leaf 12,000 lb. Ground Rating		(	(	___________

Front Shock Absorbers					(	(	___________

Integral Power Steering					(	(	___________

Slack Adjuster	s Automatic					(	(	___________

Brakes – Bendix ES165-05D					(	(	___________

Polished Aluminum Disc Wheels				(	(	___________

24.5 X 8.25 Hub Piloted

Tires – Bridgestone 11R 24.5  14G R283 Smartway		(	(	___________

Tapered King Pins with no Adjustment Required		(	(	___________

Unitized wheel hubs with permanent wheel seals		(	(	___________

# Rear Axle

Rear Axle – 40,000 lb. w/ Air Ride Susp. W/

Double Reduction						(	(	___________

Power Divider Lockout					(	(	___________

YES    NO        OFFERED

Slack Adjusters Automatic					(	(	___________

Brakes – Bendix ES165-07L					(	(	___________

Synthetic Lube						(	(	___________

Wheels – Polished Aluminum Disc 24.5 X 8.25;		(	(	___________

Hub Piloted

Tires – Bridgestone 11R 24.5 14G M726EL			(	(	___________

# Cab (Interior Features)

Ash Tray							(	(	___________

Cigar Lighter 							(	(	___________

AM/FM Radio with CD w/ Weatherband & Bluetooth	(	(	___________

Coat Hooks							(	(	___________

Dispatch Box mounted on Rear Panel			(	(	___________

Overhead Console including 3 Storage Compartments	(	(	___________

With Retaining Nets

Heater with Integral Defroster				(	(	___________

Air Conditioner						(	(	___________

Dome Lights – 2 Driver’s side, 2 Passenger Side		(	(	___________

Steering Wheel, 2 Spoke Urethane Grip

Brushed Nickel Spoked				(	(	___________

YES    NO        OFFERED

Infinitely Adjusting Steering Column	, Tilt and Telescope	(	(	___________

Seats:

Driver – Air Sears Atlas 80				(	(	___________

Air Susp. (Hi-Back)

Rider – Fixed High Back Non suspension w/

Integrated storage compartment			(	(	_______

Seat Belts – Driver and Rider Lap & Shoulder		(	(	___________

With Cab Mounted Shoulder Belt

Sun Visors – LH and RH					(	(	___________

Floor Mats – Polyurethane 			 		(	(	___________

T.M.C. Recommended Instrument Panel			(	(	___________

Driver Information Display					(	(	___________

Air Pressure Gauge – Dual					(	(	___________

Voltmeter							(	(	___________

Fuel Level Gauge						(	(	___________

Engine Oil Pressure Gauge 					(	(	___________

Exhaust Pyrometer Gauge					(	(	___________

Engine Coolant Temperature Gauge				(	(	___________

Transmission Oil Temperature Gauge			(	(	___________

Low Air Pressure Indicator (Light and Buzzer)		(	(	___________

YES    NO        OFFERED

Manifold Pressure Gauge					(	(	___________

Speedometer/Trip Odometer, Electronic			(	(	___________

Tachometer with Hourmeter, Electronic			(	(	___________

High Beam Indicator   					(	(	___________

Parking Brake On Indicator					(	(	___________

Key Type Starting						(	(	___________

Engine Shutoff – Key-Type Control				(	(	___________

Courtesy Light Switch (Head and Clearance)		(	(	___________

Directional Signal						(	(	___________

Fire Extinguisher – 5lb.					(	(	___________

Customer Interior  / Cloth w/ Vinyl Trim Seats		(	(	___________

Reflector Kit							(	(	___________

Cab (Exterior Features)

Welded Steel Shell, Galvanized				(	(	___________

Rust Preventative Procedures					(	(	___________

Vents – Screened, Fresh Air Inlet for Heater			(	(	___________

Cab Steps – Two Step Aluminum with 			(	(	___________

Self Cleaning Threads

Safety Glass Windows					(	(	___________

YES    NO        OFFERED

Aluminum frame Mounted Headache Rack			(	(	___________

Exterior Sun Visor - Stainless Steel				(	(	___________

Tinted Two piece Windshields, Side and Rear Glass		(	(	___________

Windshield Wipers – Two, Fixed Arm and Blade Type	(	(	___________

Wiper Motor – Electric (2), Two speed Intermittent		(	(	___________

Windshield Washers – Electric Wiper Mtd. with 5 qt. 	(	(	___________

(4.7 L) Translucent Reservoir

Mirrors – Aero -  Bright Finished Heated and Motorized	(	(	___________

RH & LH w/ Integrated Convex Mirror

Swing Away Arms

Headlamps – 2 Flush Mounted with Replaceable Bulb 	(	(	___________

Daytime Running Lights					(	(	___________

Identification and Clearance Lamps – Grote Premium	(	(	___________

Bright Finished

Side Markers - Lamps and Reflectors				(	(	___________

Front Turn Signals						(	(	___________

Transistorized Flasher						(	(	___________

Horns – Air, 2 Mounted each side of Cab 			(	(	___________

& Electric (Single Tone)

Doors – Galvanized Steel with:				(	(	___________

Power Windows & Door Lock

Visibility Door

YES    NO        OFFERED

Grab Handles – Aluminum, RH & LH Behind Door		(	(	___________

Cab Mounting – Dual Air Suspended Rear			(	(	___________

Dual CB Antenna Mirror Mounted				(	(	___________

Reflectors on the Back of Cab				(	(	___________

# Fuel Tank

Fuel Tank – LH 117 Gallon Aluminum			(	(	___________

RH 50 Gallon Aluminum

D.E.F. Tank – 18.4 Gallon Frame Mounted			(	(	___________

# Air Brakes

Air Dryer – Heated 1200					(	(	___________

Aluminum Air Tanks						(	(	___________

ABS System							(	(	___________

Hand Control Valve for Trailer				(	(	___________

Manual Drain Valve – Non-Heated w/Lanyards		(	(	___________

# Coiled Air Lines 						(	(	___________

Coiled Electric Lines						(	(	___________

Deck Plate							(	(	___________

YES     NO        OFFERED

# Electrical

Daytime Running Lights					(	(	___________

Polished Aluminum Battery Box Cover			(	(	___________

Electric Circuit Protection Package				(	(	___________

Fog Lights							(	(	___________

LED Tail Lights						(	(	___________

### Paint

Paint Cab & Interior – DuPont White				(	(	___________

Chassis & Running Gear – DuPont Black			(	(	___________

### Warranty

1 year / 100,000 mile Base Warranty on Chassis		(	(	___________

2 year / 250,000 mile Parts & Labor Warranty on engine	(	(	___________

“From Fan Hub to Fly-wheel” Specifically Including:

Air Compressor				(	(	___________

EGR Control Valve				(	(	___________

Fuel Injectors					(	(	___________

Exhaust After Treatment System		(	(	___________

Fuel Supply Pump				(	(	___________

Starter						(	(	___________

YES     NO        OFFERED

Turbocharger					(	(	___________

5 year / 500,000 mile Extended Warranty – 100% Parts	(	(	___________

& Service on Major Engine Components

3 year / 300,000 mile Warranty – 100% Parts & Labor 	(	(	___________

on Transmission, Axles, and Frame

Roadside Assistance & Towing –				(	(	___________

2 Year / 250,000 on Engine

1 Year / 100,000 on Transmission and Axles